## Slide 1: ECE/CS 552: ISA Advanced
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: MIPS Machine Language
All instructions are 32 bits wide
Assembly: add $1, $2, $3
Machine language:
  bit 31 bit 0
  00000000010000110000100000100000
  000000 00010 00011 00001 00000 100000
  opcode rs rt rd shamt funct
  alu-rr 2 3 1 unused add (signed)

## Slide 3: Instruction Format
Opcode (most-significant 6 bits) specifies which operation and which instruction format:
  Register (R-format)
  Immediate (I-format)
  Jump (J-format)
Depending on the format, the operand bits are interpreted differently

## Slide 4: Instruction Format
R-format
  opc rs rt rd shamt function
  6 5 5 5 5 6
Up to 3 register operands and a shift amount (for shift instructions only)
Function bits extends the opcode to specify more arithmetic operations.
  e.g., addu: opc = 0x0, function = 0x21
Most ALU ops are R-format instructions

## Slide 5: Instruction Format
Assembly: lw $1, 72($2)
Machine: 100011 00010 00001 0000000001001000
lw 2 1 72
I-format
  opc rs rt address/immediate
  6 5 5 16

## Slide 6: Instruction Format
I-format used for ALU ops with immediates
  addi $1, $2, 100
  001000 00010 00001 0000000001100100
What about constants larger than 16 bits
  Outside range: [-32768, 32767)?
  1100 0000 0000 0000 1111?
  lui $4, 12 # $4 == 0000 0000 0000 1100 0000 0000 0000 0000
  ori $4, $4, 15 # $4 == 0000 0000 0000 1100 0000 0000 0000 1111

## Slide 7: Instruction Format
All loads and stores use I-format
Branches also use I-format:
beq $1, $2, 7
000100 00001 00010 0000 0000 0000 0111
PC = PC + 4 + (7 << 2) # word offset

## Slide 8: Instruction Format
Finally, J-format:
j address
Opcode offset
6 26
Target address computation is weird in MIPS:
  target = {4 MSb of PC, offset, 00}

## Slide 9: Summary: Instruction Formats
R: opcode rs rt rd shamt function
6 5 5 5 5 6
I: opcode rs rt address/immediate
6 5 5 16
J: opcode offset
6 26

## Slide 10: Stack
Stack: parameters, return values, return address
Stack grows from higher to lower addresses (indefinitely)
$sp ($29) is stack pointer: points to top (recent) word
Push $t2:
  addi $sp, $sp, -4
  sw $t2, 0($sp)
Pop $t2:
  lw $t2, 0($sp)
  addi $sp, $sp, 4

## Slide 11: Procedure Calls
Calling convention is part of application binary interface (ABI)
  Caller
    Save registers ($t regs are caller-saved)
      Push current values of registers that you will read after the procedure returns
    Set up arguments
    Call procedure (jal)
    Get results
    Restore (pop) registers
  Callee
    Save registers ($s regs are callee-saved)
      Push current values of registers that you will (over)write within the procedure
    Perform procedure work, set up result
    Restore (pop) registers
    Return (jr $ra)

## Slide 12: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 add $t1, $a0, $t1 lw $t0, 0($t1) lw $t2, 4($t1) sw $t2, 0($t1) sw $t0, 4($t1) jr $ra

## Slide 13: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 lw $t0, 0($t1) lw $t2, 4($t1) sw $t2, 0($t1) sw $t0, 4($t1) jr $ra

## Slide 14: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) lw $t2, 4($t1) sw $t2, 0($t1) sw $t0, 4($t1) jr $ra

## Slide 15: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) sw $t2, 0($t1) sw $t0, 4($t1) jr $ra

## Slide 16: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) # [$t2] = v[k+1] sw $t2, 0($t1) sw $t0, 4($t1) jr $ra

## Slide 17: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) # [$t2] = v[k+1] sw $t2, 0($t1) # v[k] = v[k+1] sw $t0, 4($t1) # v[k+1] = temp jr $ra

## Slide 18: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) # [$t2] = v[k+1] sw $t2, 0($t1) # v[k] = v[k+1] sw $t0, 4($t1) # v[k+1] = temp jr $ra # return

## Slide 19: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) # [$t2] = v[k+1] sw $t2, 0($t1) # v[k] = v[k+1] sw $t0, 4($t1) # v[k+1] = temp jr $ra # return
What can go wrong if we use $s1 instead of $t1?

## Slide 20: Procedure Example
swap(int v[], int k) {
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# $a0 is &v[0] and $a1 is k (i.e., 1st and 2nd incoming arguments) # $t0, $t1 and $t2 are caller-saved temporaries
swap: sll $t1, $a1, 2 # [$t1] = k*4 add $t1, $a0, $t1 # [$t1] = v + k*4 = &(v[k]) lw $t0, 0($t1) # [$t0] = temp = v[k] lw $t2, 4($t1) # [$t2] = v[k+1] sw $t2, 0($t1) # v[k] = v[k+1] sw $t0, 4($t1) # v[k+1] = temp jr $ra # return
What can go wrong if we use $s1 instead of $t1?
lw $s1, 0($t2)
jal swap
add $t3, $s4, $s1

## Slide 21: Addressing Modes
There are many ways of accessing operands
Register addressing:
add $1, $2, $3
op
rs
rt
rd
. . .
funct
register

## Slide 22: Addressing Modes
Base addressing (aka displacement)
lw $1, 100($2) # $2 == 400, M[500] == 42
op
rs
rt
Offset/displacement
register
Memory
Effective
address
500
400
100

## Slide 23: Addressing Modes
Immediate addressing
addi $1, $2, 100
op
rs
rt
immediate

## Slide 24: Addressing Modes
PC relative addressing
beq $1, $2, 100 # if ($1==$2) PC = PC + 4 + 100
op
rs
rt
address
PC
Memory
Effective
address

## Slide 25: Addressing Modes
Not found in MIPS:
  Indexed: add two registers – M[base + index]
  Indirect: M[M[addr]] – two memory references
  Autoincrement/decrement: add operand size
  Autoupdate – found in PowerPC, PA-RISC
    Like displacement, but update base register

## Slide 26: Addressing Modes
Autoupdate
lwupdate $1,24($2) # $1 = M[$2+24]; $2 = $2 + 24
op
rs
rt
address
register
Memory
Effective
address
Delay

## Slide 27: Addressing Modes
for(i=0; i < N, i += 1)
sum += A[i];
# $s0 is sum, $s1 is &A[i]
Original loop: Loop with autoupdate:
lw $2, 0($s1) lwupdate $2, 4($s1)
addi $s1, $s1, 4 add $s0, $s0, $2
add $s0, $s0, $2
But need to be careful:
With autoupdate, need sub $s1, $s1, 4 before the loop

## Slide 28: Endianness
How bytes within a word are addressed
Big endian: LS byte at address xxxxxx11 (binary)
  E.g. IBM, SPARC
Little endian: LS byte at address xxxxxx00 (binary)
  E.g. Intel x86, our MIPS ISA
Some architectures support a switch for both
Causes headaches for
  Ugly pointer arithmetic
  Multibyte datatype transfers from one machine to another

## Slide 29: Endianness
All instructions are 32 bits wide
Assembly: add $1, $2, $3
Machine language:
  bit 31 bit 0
  00000000010000110000100000100000
  000000 00010 00011 00001 00000 100000
Little endian | 
addr 00 | 0x20
addr 01 | 0x08
addr 10 | 0x43
addr 11 | 0x00
Big endian | 
addr 00 | 0x00
addr 01 | 0x43
addr 10 | 0x08
addr 11 | 0x20

## Slide 30: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  int i = 0;
  do {
  sum += A[i];
  i++;
  } while (i < N);
  addi $s0, $zero, ___
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  ___ $s1, $zero, 64
  LOOP: sll $t2, $t1, ___
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, ___, $t3
  addi $t1, $t1, 1
  slt $t4, ___, ___
  bne $t4, $zero, LOOP

## Slide 31: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  int i = 0;
  do {
  sum += A[i];
  i++;
  } while (i < N);
  addi $s0, $zero, ___
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  ___ $s1, $zero, 64
  LOOP: sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, ___, $t3
  addi $t1, $t1, 1
  slt $t4, ___, ___
  bne $t4, $zero, LOOP

## Slide 32: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  int i = 0;
  do {
  sum += A[i];
  i++;
  } while (i < N);
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  ___ $s1, $zero, 64
  LOOP: sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, ___, $t3
  addi $t1, $t1, 1
  slt $t4, ___, ___
  bne $t4, $zero, LOOP

## Slide 33: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  int i = 0;
  do {
  sum += A[i];
  i++;
  } while (i < N);
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  ___ $s1, $zero, 64
  LOOP: sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  slt $t4, ___, ___
  bne $t4, $zero, LOOP

## Slide 34: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  int i = 0;
  do {
  sum += A[i];
  i++;
  } while (i < N);
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 64
  LOOP: sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  slt $t4, $t1, $s1
  bne $t4, $zero, LOOP

## Slide 35: Exercise – MIPS Assembly
Does the assembly correspond to the C code?
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 64
  LOOP: sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  slt $t4, $t1, $s1
  bne $t4, $zero, LOOP

## Slide 36: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 64
  LOOP: slt $t4, $t1, $s1
  ___ $t4, $zero, ___
  sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  ___ LOOP
  EXIT:

## Slide 37: Exercise – MIPS Assembly
Fill in the blanks:
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 64
  LOOP: slt $t4, $t1, $s1
  beq $t4, $zero, EXIT
  sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  j LOOP
  EXIT:

## Slide 38: Exercise – MIPS Assembly
Reduce the number of instructions executed?
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 64
  LOOP: slt $t4, $t1, $s1
  beq $t4, $zero, EXIT
  sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($t2)
  add $t0, $t0, $t3
  addi $t1, $t1, 1
  j LOOP
  EXIT:

## Slide 39: Exercise – MIPS Assembly
Reduce the number of instructions executed?
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  add $t1, $zero, $zero
  addi $s1, $zero, 512
  LOOP: slt $t4, $s0, $s1
  beq $t4, $zero, EXIT
  sll $t2, $t1, 2
  add $t2, $t2, $s0
  lw $t3, 0($s0)
  add $t0, $t0, $t3
  addi $s0, $s0, 4
  j LOOP
  EXIT:

## Slide 40: Exercise – MIPS Assembly
Reduce the number of instructions executed?
  // N set to 64
  int A[N]; // &A[0] = 0x100
  int sum = 0;
  for (int i = 0; i < N; i++) {
  sum += A[i];
  }
  addi $s0, $zero, 256
  add $t0, $zero, $zero
  addi $s1, $zero, 512
  LOOP: slt $t4, $s0, $s1
  beq $t4, $zero, EXIT
  lw $t3, 0($s0)
  add $t0, $t0, $t3
  addi $s0, $s0, 4
  j LOOP
  EXIT: