## Slide 1: ECE/CS 552: Arithmetic Logic Units
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Datatypes
32-bit word: b31 b30 … b3 b2 b1 b0
  Recall: n bits enables 2n unique combinations
No inherent meaning
  In isolation, all bits in registers and memory are just arbitrary
  Instructions define datatypes by how they use the bits
For example:
If [$t0] = 10101101001010000000000000000000, then:
  $t0 may contain an integer value: -1389887488
  $t0 may contain an unsigned integer value: 2905079808
  $t0 may contain a memory address: 0xAD280000
  $t0 may contain a machine instruction: sw $t0, 0($t1)

## Slide 3: Signed Integers
Consider a signed 8-bit number
  -b7 x 27 + … b1 x 21 + b0 x 20
11000001
  -27 + 26 + 20 = -128 + 64 + 1 = -63
11101010
  -27 + 26 + 25 + 23 + 21 = -128 + 64 + 32 + 8 + 2 = -22

## Slide 4: Exercise – MIPS Assembly
What does this assembly code do?
  nor $t0, $t0, $zero
  addi $t0, $t0, 1

## Slide 5: Exercise – MIPS Assembly
What does this assembly code do?
  nor $t0, $t0, $zero # [$t0] = ~[$t0] …
  addi $t0, $t0, 1 # … + 1

## Slide 6: Exercise – MIPS Assembly
What does this assembly code do?
  nor $t0, $t0, $zero # [$t0] = ~[$t0] …
  addi $t0, $t0, 1 # … + 1
Negates integer in $t0
Reduce the number of instructions executed?

## Slide 7: Exercise – MIPS Assembly
What does this assembly code do?
  sub $t0, $zero, $t0 # [$t0] = 0 – [$t0]
Negates integer in $t0
Reduce the number of instructions executed?