## Slide 1: ECE/CS 552: Arithmetic Logic Units
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Basic Arithmetic and the ALU
Signed/unsigned integers
Addition/subtraction
ALUs
Overflow

## Slide 3: Basic Arithmetic and the ALU
Covered later in the semester:
  Integer multiplication, division
  Floating point arithmetic
These are not crucial for the project

## Slide 4: Background
32-bit word: b31 b30 … b3 b2 b1 b0
  Recall: n bits enables 2n unique combinations
No inherent meaning
  In isolation, all bits in registers and memory are just arbitrary
  Instructions define datatypes by how they use the bits
For example:
If [$t0] = 10101101001010000000000000000000, then:
  $t0 may contain an integer value: -1389887488
  $t0 may contain an unsigned integer value: 2905079808
  $t0 may contain a memory address: 0xAD280000
  $t0 may contain a machine instruction: sw $t0, 0($t1)
    Aside: What MIPS instruction is 0x00000000?

## Slide 5: Unsigned Integers
f(b31…b0) = b31 x 231 + … + b1 x 21 + b0 x 20
Treat as normal binary number
  E.g. 0…011010101
  = 1 x 27 + 1 x 26 + 0 x 25 + 1 x 24 + 0 x 23 + 1 x 22 + 0 x 21 + 1 x 20
  = 128 + 64 + 16 + 4 + 1 = 213
Max f(111…11) = 232 – 1 = 4,294,967,295
Min f(000…00) = 0
Range [0,232-1]

## Slide 6: Signed Integers
2’s complement
  f(b31…b0) = -b31 x 231 + … b1 x 21 + b0 x 20
Max f(0111…11) = 231 – 1 = 2147483647
Min f(100…00) = -231 = -2147483648 (asymmetric)
Range[-231,231-1]
Invert bits and add one: e.g. –6
  000…0110 => 111…1001 + 1 => 111…1010

## Slide 7: Signed Integers
Consider a signed 8-bit number
  -b7 x 27 + … b1 x 21 + b0 x 20
11110001
  -27 + 26 + 25 + 24 + 20 = -128 + 64 + 32 + 16 + 1 = -15

## Slide 8: Sign Extension
Convert signed 8-bit integer to 16-bit integer?
Copy MSB bit[7] to bits [15:8]
What does 11110001 become?
1111111111110001
How about 01110001?
0000000001110001
Why does sign extension work for negative numbers?

## Slide 9: Sign Extension
Convert signed 4 bit to signed 5 bit
Copy the MSB: 1001  11001
1001 = -8 + 1 = -7
11001 = -16 + 8 + 1 = -7
-8
The old negative MSB becomes positive, and the new negative MSB offsets for zero sum

## Slide 10: Why 2’s Complement
Why not use sign-magnitude?
  2’s complement makes hardware simpler
  Representation affects ease of calculation, not correctness of answer
000
001
010
011
100
101
110
111
0
1
2
3
-4
-3
-2
-1
000
001
010
011
100
101
110
111
0
1
2
3
-0
-1
-2
-3
2’s complement
sign-magnitude

## Slide 11: Addition
4-bit unsigned example
4-bit signed example
0 | 0 | 1 | 1 |  | 3
1 | 0 | 1 | 0 |  | 10
1 | 1 | 0 | 1 |  | 13
0 | 0 | 1 | 1 |  | 3
1 | 0 | 1 | 0 |  | -6
1 | 1 | 0 | 1 |  | -3
+
+

## Slide 12: Subtraction
A – B = A + -B = A + 2’s complement of B
e.g. 3 – 2 = 3 + -2 = 1
0 | 0 | 1 | 1 |  | 3
1 | 1 | 1 | 0 |  | -2
0 | 0 | 0 | 1 |  | 1
+

## Slide 13: Full Adder
Full adder (a,b,cin) => (cout, s)
cout = two or more of (a, b, cin)
s = exactly one or three of (a,b,cin)
a | b | cin | cout | s
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 14: Ripple-carry Adder
Just concatenate the full adders
Full
Add
er
a
0
b
0
Full
Add
er
a
2
b
2
Full
Add
er
a
1
b
1
Full
Add
er
a
31
b
31
c
in
C
out

## Slide 15: Ripple-carry Subtractor
A – B = A + (-B) => invert B and set cin to 1
Full
Add
er
a
0
b
0
C
out
1
Full
Add
er
a
1
b
1
Full
Add
er
a
2
b
2
Full
Add
er
a
3
b
3

## Slide 16: Combined Ripple-carry Adder/Subtractor
Op = 1 => subtract
XOR B with control and set cin0 to Op
Full
Add
er
a
0
b
0
Full
Add
er
a
1
b
1
Full
Add
er
a
2
b
2
Full
Add
er
a
31
b
31
Op
C
out

## Slide 17: Logical Operations
Bitwise AND, OR, XOR, NOR
  Implement w/ 32 gates in parallel
Shifts and rotates
  sll -> shift left logical (LSb := 0)
  srl -> shift right logical (MSb := 0)
  sra -> shift right arithmetic (new MSb := old MSb)
  rol => rotate left (LSb := MSb)
  ror => rotate right (MSb := LSb)

## Slide 18: Shifter
x7
x6
x5
x4
x3
x2
x1
x0
s0
s1
s2
Shift by 1
Shift by 2
Shift by 4
Right shift logic shown: missing inputs are 0
  Left shift logic similar
Rotate: wraparound instead of 0 inputs

## Slide 19: Simple ALU
Add
operation
carry
in
invert
result
a
b
M
u
x
M
u
x

## Slide 20: Overflow
With n bits, overflow occurs when result is beyond 2n possible values
  Unsigned range [0, 2n-1]
  2’s complement range [-2n-1, 2n-1-1]
e.g., 3-bit unsigned add
5 + 6 > max value (7): 101 + 110 => 1011
f(3:0) = a(2:0) + b(2:0) => f(3) is overflow
  Carry-out from most-significant bit signals overflow

## Slide 21: Addition Overflow
More complicated for 2’s complement
  Can we just use the carry-out of MSb?
e.g., 3-bit signed add
-1 + -1 = -2:
111 + 111 = 1110
110 = -2 is correct, no overflow despite carry-out

## Slide 22: Addition Overflow
When is overflow NOT possible?
  (p1, p2) > 0 and (n1, n2) < 0
  p1 + p2 maybe?
  p1 + n1 not possible
  n1 + p2 not possible
  n1 + n2 maybe?
Just checking signs of inputs is not sufficient

## Slide 23: Addition Overflow
2 + 3 = 5 > 3: 010 + 011 = 101 (–3)
  Sum of two positive numbers should not be negative
    Conclude: overflow
-1 + -4 = -5 < -4: 111 + 100 = 011 (+3)
  Sum of two negative numbers should not be positive
    Conclude: overflow
Notes: Let’s apply what we’ve learned with some signed 3-bit examples. Say we’re adding 2+3. We know the sum is 5, which would be 0101 with 4 bits, but signed 3 bit math results in 101 or negative 3. We have a new rule: if we sum 2 positive numbers and the result is negative, we know an overflow happened.
Let’s consider a similar, but opposite situation with -1 + -4. If we had 4-bits, the result should be 1011 but we only get the bottom 3 bits which is 011, or positive 3. Since the sum of 2 negative numbers resulted in a positive number, we can conclude that an overflow occurred.

## Slide 24: Addition Overflow
Consider MSb full adder (a,b,cin) => (cout, s)
When does overflow happen?
ai | bi | cin | cout | si
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 25: Subtraction Overflow
No overflow on a – b if signs are the same
Neg – pos => neg; overflow otherwise
Pos – neg => pos; overflow otherwise

## Slide 26: What to do on Overflow?
Ignore ! (C language semantics)
  What about Java? (try/catch?)
Flag – condition code
Sticky flag – e.g. for floating point
  Otherwise gets in the way of fast hardware
Trap – possibly maskable
  MIPS has e.g. add that traps, addu that does not
  Useful for extended precision in software

## Slide 27: Combined Ripple-carry Adder/Subtractor
Ripple-carry is too slow
  Gate delays = 32 * FA + XOR
Full
Add
er
a
0
b
0
Full
Add
er
a
1
b
1
Full
Add
er
a
2
b
2
Full
Add
er
a
31
b
31
add/sub
C
out

## Slide 28: Carry Lookahead
Theoretically, in parallel:
  Sum0 = f(cin, a0, b0)
  Sumi = f(cin, ai…a0,, bi…b0)
  Sum31 = f(cin, a31…a0, b31…b0)

## Slide 29: Carry Lookahead
0101 0100
0011 0110
Need:
both 1s to generate carry
one or both 1s to propagate carry
Define: gi = ai * bi ## carry generate
pi = ai + bi ## carry propagate
Carryin: ci+1 = ai * bi + ai * ci + bi * ci
= ai * bi + (ai + bi) * ci
= gi + pi * ci

## Slide 30: Carry Lookahead
Therefore:
c1 = g0 + p0 * c0
c2 = g1 + p1 * c1 = g1 + p1 * (g0 + p0 * c0)
= g1 + p1 * g0 + p1 * p0 * c0
c3 = g2 + p2 * g1 + p2 * p1 * g0 + p2 * p1 * p0 * c0
c4 = g3 + p3*g2 + p3*p2*g1 + p3*p2*p1*g0 + p3*p2*p1*p0*c0
1 gate delay (for gi, pi) + 2 gate delays (for ci+1)
But needs large i+1 fan-in for the OR and rightmost AND in ci

## Slide 31: 4-bit Carry Lookahead Adder
p
3
g
3
a
3
b
3
s
3
c
3
p
2
g
2
a
2
b
2
s
2
c
2
p
1
g
1
a
1
b
1
s
1
c
1
p
0
g
0
a
0
b
0
s
0
c
0
Carry Lookahead Block
c
0
c
4

## Slide 32: Hierarchical CLA for 16 bits
P
G
a,b
12-15
s
12-15
c
12
P
G
a,b
8-11
s
8-11
c
8
P
G
a
4-7
b
4-7
s
4-7
c
4
P
G
a
0-3
b
0-3
s
0-3
c
0
Carry Lookahead Block
c
0
c
15
4-bit CLA
4-bit CLA
4-bit CLA
4-bit CLA

## Slide 33: Hierarchical CLA for 16 bits
Build 16-bit adder from four 4-bit adders
Figure out G and P for 4 bits together
G0,3 = g3 + p3 * g2 + p3 * p2 * g1 + p3 * p2 * p1 * g0
P0,3 = p3 * p2 * p1 * p0
G4,7 = g7 + p7 * g6 + p7 * p6 * g5 + p7 * p6 * p5 * g4
P4,7 = p7 * p6* p5 * p4
…
G12,15 = g15 + p15 * g14 + p15* p14 * g13 + p15 * p14 * p13 * g12
P12,15 = p15 * p14 * p13 * p12

## Slide 34: Exercise – ALU
1-bit 2-input ALU. Assume CarryIn=0.
  Operation = 0 (AND), 1 (OR), 2 (ADD)
  Can invert the two inputs

## Slide 35: Exercise – ALU
1-bit 2-input ALU. Assume CarryIn=0. How to compute Result = NOR(a, b)?
  Ainvert = ?, Binvert = ?, Operation = ?

## Slide 36: Exercise – ALU
1-bit 2-input ALU. Assume CarryIn=0. How to compute Result = NOR(a, b)?
  Ainvert = 1, Binvert = 1, Operation = 0

## Slide 37: Exercise – ALU
1-bit 2-input ALU. Assume CarryIn=0. How to compute Result = XNOR(a, b)?
  Ainvert = ?, Binvert = ?, Operation = ?

## Slide 38: Exercise – ALU
1-bit 2-input ALU. Assume CarryIn=0. How to compute Result = XNOR(a, b)?
  Ainvert = 1 (or 0), Binvert = 0 (or 1), Operation = 2

## Slide 39: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8

## Slide 40: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8
  srl $t0, $s0, 31
  beq $t0, $zero, SKIP
  addi $t0, $zero, -1
  sll $t0, $t0, 24
  or $s1, $t0, $s1
  SKIP:

## Slide 41: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31
  beq $t0, $zero, SKIP
  addi $t0, $zero, -1
  sll $t0, $t0, 24
  or $s1, $t0, $s1
  SKIP:

## Slide 42: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31 # [$t0] = sign([$s0])
  beq $t0, $zero, SKIP
  addi $t0, $zero, -1
  sll $t0, $t0, 24
  or $s1, $t0, $s1
  SKIP:

## Slide 43: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31 # [$t0] = sign([$s0])
  beq $t0, $zero, SKIP
  addi $t0, $zero, -1 # [$t0] = all 1s
  sll $t0, $t0, 24 # [$t0] = 8 leading 1s
  or $s1, $t0, $s1 # [$s1] |= 8 leading 1s
  SKIP:

## Slide 44: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31 # [$t0] = sign([$s0])
  sll $t0, $t0, 24 # [$t0] = sign * 224=32-8
  sub $t0, $zero, $t0 # [$t0] = 8 leading signs
  or $s1, $t0, $s1 # [$s1] |= 8 leading signs
  Negating a power of two (00100) flips leading 0s (11100)

## Slide 45: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31 # [$t0] = sign([$s0])
  sll $t0, $t0, 24 # [$t0] = sign * 224=32-8
  sub $t0, $zero, $t0 # [$t0] = 8 leading signs
  add $s1, $t0, $s1 # [$s1] += 8 leading signs

## Slide 46: Exercise – SRL vs SRA
Modify the code below (using only the MIPS core instruction set) to perform arithmetic right-shift (sra) instead:
  srl $s1, $s0, 8 # [$s1] = abs([$s0]) / 28
  srl $t0, $s0, 31 # [$t0] = sign([$s0])
  sll $t0, $t0, 24 # [$t0] = sign * 224=32-8
  sub $s1, $s1, $t0 # [$s1] += 8 leading signs