## Slide 1: ECE/CS 552: Single-Cycle Data Path
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Forecast
Simple processor implementation
  Heart of 552
  Key to project
Forecast:
  Sequential logic design review
  Single-cycle data path (1 CPI)
    Fetch, ALU, load/store, branch, register file

## Slide 3: Sequential Logic Review
Logic is combinational if output is solely a function of the inputs
  e.g., ALU in previous lecture
Logic is sequential or “has state” if output is a function of:
  Past and current inputs
  Past inputs remembered in “state”

## Slide 4: Sequential Logic Review
Level-sensitive D latch:
  Clock high: Q = D and ~Q = ~D, transparent
  Clock low: Q and ~Q remain unchanged

## Slide 5: Sequential Logic Review
Master-slave D flip-flop (DFF):
  Opaque except at falling (in example) clock edge
  Falling edge: QM stores D and QS passes it through
  Rising edge: QM propagates to QS, Q unchanged
master
slave

## Slide 6: Sequential Logic Review
Why can this fail for a latch?
  Latch is transparent when clock is high
  Creates combinational loop
  Increments an indefinite number of times
D FF
+1

## Slide 7: Clocking Methodology
Use fully synchronous design in this course
  Motivation: simplifies design process
    Can guarantee timing correctness; design data and control without considering clock
  Only flip-flops, all with same clock and same edge
  All logic finishes within cycle

## Slide 8: Single-Cycle Data Path

## Slide 9: Fetch Instructions
Fetch instruction, then increment PC
  Same for all insns
Initially, let’s assume:
  PC updated every cycle
  No branches or jumps
After this instruction, fetch next one

## Slide 10: ALU Instructions
and $1, $2, $3 # [$1] = [$2] & [$3]
MIPS R-format
  opcode rs rt rd shamt function

## Slide 11: Load/Store Instructions
lw $1, immed($2) # [$1] = M[SE(immed)+[$2]]
MIPS I-format:
  opcode rs rt immed

## Slide 12: Load/Store Instructions
lw $1, immed($2) # [$1] = M[SE(immed)+[$2]]
MIPS I-format:
  opcode rs rt immed

## Slide 13: Load/Store Instructions
lw $1, immed($2) # [$1] = M[SE(immed)+[$2]]
MIPS I-format:
  opcode rs rt immed

## Slide 14: Load/Store Instructions
lw $1, immed($2) # [$1] = M[SE(immed)+[$2]]
MIPS I-format:
  opcode rs rt immed

## Slide 15: Branch Instructions
beq $1, $2, addr # if ($1==$2) [PC] = [PC] + 4 + addr<<2
Implementation:
  next = [PC] + 4
  target = next + SE(addr << 2)
  if (([$1] – [$2]) == 0)
    [PC] = target // branch taken
  else
    [PC] = next // branch not taken

## Slide 16: Branch Instructions

## Slide 17: Register File
en
D
Q
write register
read register 1
read register 2
write data
bitline
read data 1
bitline
read data 2
bitline
one-hot
decoder
one-hot
decoder
one-hot
decoder
DFF
DFF
DFF
2 read ports, 1 write port
r1
r2
31
31
0
0
5
5
5
wordline

## Slide 18: All Together

## Slide 19: Exercise
If ALUSrc stuck at 1, add $t0, $t1, $t2 correct?
0
1

## Slide 20: Exercise
If ALUSrc stuck at 1, add $t0, $t1, $t2 correct?
  No, would compute: [$t0] = [$t1] + 0x4020
0
1

## Slide 21: Exercise
If ALUSrc stuck at 1, sw $t0, 8($t1) correct?
0
1

## Slide 22: Exercise
If ALUSrc stuck at 1, sw $t0, 8($t1) correct?
  Yes
0
1