## Slide 1: ECE/CS 552: Single-Cycle Control Path
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Single-Cycle Processor
Data path:
  Combinational logic, I-mem, reg file, D-mem, PC reg
Control path:
  Just combinational logic
  Inputs into global control logic:
    Instruction word (output of I-mem)
  Outputs of global control logic:
    Select signals of muxes
    Read/write-enable signals of mem and regs
    ALU operation

## Slide 3: Global Control
For fast control logic:
  Divide up logic on a “need to know” basis
  Logic with fewer inputs is faster

## Slide 4: Global Control
R-format: opcode rs rt rd shamt function
    6 5 5 5 5 6
I-format: opcode rs rt address/immediate
    6 5 5 16
J-format: opcode address
    6 26
Inputs to register file:
  Read reg 1 = instruction[25:21]
  Read reg 2 = instruction[20:16]
  Write reg = I-format ? instruction[20:16] : instruction[15:11]
Instruction[31:26] (opcode) used for other control signals
Instruction[5:0] (function) used for ALU operation

## Slide 5: Global Control

## Slide 6: Global Control
RegDst:
0, if I-format
1, else

## Slide 7: Global Control
RegWrite:
0, if store or branch
1, else

## Slide 8: Global Control
MemRead:
1, if load
0, else

## Slide 9: Global Control
MemWrite:
1, if store
0, else

## Slide 10: Global Control
MemToReg:
1, if load
0, else

## Slide 11: Global Control
PCSrc:
1, if branch taken
0, else

## Slide 12: Global Control
ALUSrc:
0, if R-format or branch
1, else

## Slide 13: Global Control
ALU control:
f(opcode, function)

## Slide 14: ALU Control
Assume ALU control lines:
0000 | and
0001 | or
0010 | add
0110 | sub
0111 | slt (set less than)
… | ignore for now

## Slide 15: ALU Control
ALU control lines = f(opcode, function)
Instruction | Operation | Opcode | Function
add | add | 000000 | 100000
sub | sub | 000000 | 100010
and | and | 000000 | 100100
or | or | 000000 | 100101
slt | slt | 000000 | 101010

## Slide 16: ALU Control
ALU control lines = f(opcode, function)
Instruction | Operation | Opcode | Function
add | add | 000000 | 100000
sub | sub | 000000 | 100010
and | and | 000000 | 100100
or | or | 000000 | 100101
slt | slt | 000000 | 101010
lw | add | 100011 | xxxxxx
sw | add | 101011 | xxxxxx
beq | sub | 000100 | xxxxxx
4 bits
6 bits
6 bits
Simplify:
ALUOp = f(opcode)

## Slide 17: ALU Control
ALU control lines = f(ALUOp, function)
Instruction | Operation | ALUOp | Function
add | add | 10 | 100000
sub | sub | 10 | 100010
and | and | 10 | 100100
or | or | 10 | 100101
slt | slt | 10 | 101010
lw | add | 00 | xxxxxx
sw | add | 00 | xxxxxx
beq | sub | 01 | xxxxxx
4 bits
2 bits
6 bits

## Slide 18: Global Control

## Slide 19: Global Control
beq:
PCSrc = 1, if branch taken
PCSrc = Branch & Zero

## Slide 20: Exercise
Assume only these instructions supported
  ALUSrc = ?
Instruction | Operation | Opcode
add | add | 000000
sub | sub | 000000
and | and | 000000
or | or | 000000
slt | slt | 000000
lw | add | 100011
sw | add | 101011
beq | sub | 000100

## Slide 21: Exercise
Assume only these instructions supported
  ALUSrc = opcode[0] = instruction[26]
Instruction | Operation | Opcode
add | add | 000000
sub | sub | 000000
and | and | 000000
or | or | 000000
slt | slt | 000000
lw | add | 100011
sw | add | 101011
beq | sub | 000100

## Slide 22: Exercise
Assume only these instructions supported
  RegWrite = ?
Instruction | Operation | Opcode
add | add | 000000
sub | sub | 000000
and | and | 000000
or | or | 000000
slt | slt | 000000
lw | add | 100011
sw | add | 101011
beq | sub | 000100

## Slide 23: Exercise
Assume only these instructions supported
  RegWrite = ~opcode[2] & ~opcode[3]
Instruction | Operation | Opcode
add | add | 000000
sub | sub | 000000
and | and | 000000
or | or | 000000
slt | slt | 000000
lw | add | 100011
sw | add | 101011
beq | sub | 000100

## Slide 24: Global Control
More complex with entire MIPS instruction set
  Need more systematic structure
  Want to share gates between control signals
Common solution: programmable logic array
  MIPS opcodes designed to minimize PLA inputs, minterms and outputs

## Slide 25: PLA
In AND-plane, AND selected inputs to get minterms
In OR-plane, OR selected minterms to get outputs
e.g.,

## Slide 26: Global Control
Jump (j) instruction?

## Slide 27: Global Control
Jump (j) instruction?
Jump:
1, if jump instruction
0, else

## Slide 28: Single-Cycle Processor
Critical path: probably load instruction
  I-mem, reg-read, ALU, D-mem, reg-write
Other common instructions are much faster
  e.g., R-format: skip D-mem
Problem: high instruction variation
  Much worse for full instruction set and real implementation
    e.g., floating-point arithmetic
    e.g., cache misses (later)
Instructions
Cycles
Program
Instruction
Time
Cycle
(dyn insns)
X
X
(CPI)
(clock period)
worst-case

## Slide 29: Single-Cycle Processor
Solution:
  Variable clock period per instruction?
    Too hard to control/build
Instructions
Cycles
Program
Instruction
Time
Cycle
(dyn insns)
X
X
(CPI)
(clock period)

## Slide 30: Single-Cycle Processor
Solution:
  Variable clock period per instruction?
    Too hard to control/build
  Variable cycles per instruction
    Fixed short clock period
    Break data path into multicycle stages
Instructions
Cycles
Program
Instruction
Time
Cycle
(dyn insns)
X
X
(CPI)
(clock period)

## Slide 31: Exercise
If RegDst stuck at 0, sub $t0, $t1, $t2 correct?

## Slide 32: Exercise
If RegDst stuck at 0, sub $t0, $t1, $t2 correct?
  No, would compute: [$t2] = [$t1] - [$t2]