## Slide 1: ECE/CS 552: Data Hazards
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill and John Shen

## Slide 2: Pipeline Hazards
Forecast:
  Program Data Dependences
  Pipeline Data Hazards
    Stalls
    Forwarding and bypassing
Next lecture:
  Program Control Dependences
  Pipeline Control Hazards
  Exceptions

## Slide 3: Program Data Dependences
True dependence
  Read-after-write (RAW): Y reads what X writes
  Y cannot execute until X produces its result
Anti-dependence
  Write-after-read (WAR): Y overwrites what X reads
  Y cannot write its result until X has read its sources
Output dependence
  Write-after-write (WAW): Y overwrites what X writes
  Y cannot write its result until X has written its result

## Slide 4: Program Data Dependences
e.g., List all RAW register dependences:
  I1→I2, $s3
  I2→I3, $s2
  I2→I4, $s2
  I3→I4, $s3
I0: | sw | $s1, 0($s3)
I1: | add | $s3, $s1, $s0
I2: | lw | $s2, 4($s3)
I3: | lw | $s3, 0($s2)
I4: | beq | $s3, $s2, TARGET

## Slide 5: Program Data Dependences
e.g., List all WAR register dependences:
  I0→I1, $s3
  I0→I3, $s3
  I2→I3, $s3
I0: | sw | $s1, 0($s3)
I1: | add | $s3, $s1, $s0
I2: | lw | $s2, 4($s3)
I3: | lw | $s3, 0($s2)
I4: | beq | $s3, $s2, TARGET

## Slide 6: Program Data Dependences
e.g., List all WAW register dependences:
  I1→I3, $s3
I0: | sw | $s1, 0($s3)
I1: | add | $s3, $s1, $s0
I2: | lw | $s2, 4($s3)
I3: | lw | $s3, 0($s2)
I4: | beq | $s3, $s2, TARGET

## Slide 7: Pipeline Data Hazards
What are pipeline hazards?
  Potential violations of program dependences
  Must ensure program dependences are not violated
How to resolve?
  Static: compiler/programmer guarantees correctness
  Dynamic: processor hardware checks at runtime

## Slide 8: Pipeline Data Hazards
Which data hazards are possible in IF-ID-EX-MEM-WB pipeline?
  Multiple instructions in-flight at the same time
  Can a RAW register dependence be a hazard?

## Slide 9: Pipeline Data Hazards
e.g., RAW register data dependence:
  Hazard: when sub is reading [$1] in ID stage, add is still in EX stage and has not written the new value of [$1] to the register file yet
  add $1, $2, $3
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D | X | M | W |  |  |  |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  |  |  |  | 

## Slide 10: Pipeline Data Hazards
Which data hazards are possible in IF-ID-EX-MEM-WB pipeline?
  Multiple instructions in-flight at the same time
  Can a RAW register dependence be a hazard?
    Yes
  Can a WAR register dependence be a hazard?

## Slide 11: Pipeline Data Hazards
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D | X | M | W |  |  |  |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  |  |  |  | 
e.g., WAR register data dependence:
  Not a hazard: every instruction performs WB after ID, so a later instruction will never write a register (WB) before an earlier instruction’s read (ID)
  add $1, $2, $3
  sub $3, $4, $5

## Slide 12: Pipeline Data Hazards
Which data hazards are possible in IF-ID-EX-MEM-WB pipeline?
  Multiple instructions in-flight at the same time
  Can a RAW register dependence be a hazard?
    Yes
  Can a WAR register dependence be a hazard?
    No
  Can a WAW register dependence be a hazard?

## Slide 13: Pipeline Data Hazards
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D | X | M | W |  |  |  |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  |  |  |  | 
e.g., WAW register data dependence:
  Not a hazard: instructions perform WB in order, so a younger instruction will never write a register (WB) before an older instruction’s write (WB)
  add $1, $2, $3
  sub $1, $4, $5

## Slide 14: Pipeline Data Hazards
unless writing to executable memory region (ignore for this course)
Register data hazards
  RAW: Yes/No?
  WAR: Yes/No?
  WAW: Yes/No?
Memory data hazards
  RAW: Yes/No?
  WAR: Yes/No?
  WAW: Yes/No?

## Slide 15: Resolving RAW Hazards
Step 1: Detect hazard at ID stage
  Compare control signals of other stages

## Slide 16: Resolving RAW Hazards
Step 1: Detect hazard at ID stage
  Compare control signals of other stages
  Hazard if:
    ID/EX.WriteRegister == IF/ID.RegisterRs, or
    ID/EX.WriteRegister == IF/ID.RegisterRt
  add $1, $2, $3
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add | F | D | X | M | W |  |  |  | 
sub |  | F | D | X | M | W |  |  | 
*WriteRegister = R-format ? RegisterRd : RegisterRt

## Slide 17: Resolving RAW Hazards
Step 1: Detect hazard at ID stage
  Compare control signals of other stages
  Hazard if:
    EX/MEM.WriteRegister == IF/ID.RegisterRs, or
    EX/MEM.WriteRegister == IF/ID.RegisterRt
  add $1, $2, $3
  …
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add | F | D | X | M | W |  |  |  | 
… |  |  |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  | 
*WriteRegister = R-format ? RegisterRd : RegisterRt

## Slide 18: Resolving RAW Hazards
Step 1: Detect hazard at ID stage
  Compare control signals of other stages
  Hazard if:
    MEM/WB.WriteRegister == IF/ID.RegisterRs, or
    MEM/WB.WriteRegister == IF/ID.RegisterRt
  add $1, $2, $3
  …
  …
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add | F | D | X | M | W |  |  |  | 
… |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  | 
sub |  |  |  | F | D | X | M | W | 
*WriteRegister = R-format ? RegisterRd : RegisterRt

## Slide 19: Resolving RAW Hazards
Actually need to check for more conditions:
  WriteRegister not necessarily used (e.g., sw)
  RegisterRs/RegisterRt not necessarily read (e.g., addi, jump)
    e.g., Not a RAW dependence:
*WriteRegister = R-format ? RegisterRd : RegisterRt
  sw $1, 0($2)
  sub $4, $5, $1

## Slide 20: Resolving RAW Hazards
Step 2a: Stall the reader instruction at ID stage
  Instructions in IF and ID stay there for next cycle
  Send nop (no operation, or bubble) ahead of reader until hazard is resolved
  add $1, $2, $3
  sub $4, $5, $1
  lw $6, 0($7)
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
sub |  | F | D* | D* | D* | D | X | M | W | 
lw |  |  | F* | F* | F* | F | D | X | M | W

## Slide 21: Resolving RAW Hazards
  add $1, $2, $3
  sub $4, $5, $1
  lw $6, 0($7)
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
sub |  | F | D* | D* | D* | D | X | M | W | 
lw |  |  | F* | F* | F* | F | D | X | M | W
add
cycle 1:
add
sub
cycle 2:
sub
lw
add
cycle 3:
sub
lw
nop
cycle 4:
add
sub
lw
nop
cycle 5:
nop
add
sub
lw
nop
cycle 6:
nop
nop
lw
sub
cycle 7:
nop
nop

## Slide 22: Resolving RAW Hazards
To stall an instruction at the ID stage:
  Disable PCWrite and IF/IDWrite
  Clear ID/EX control signals to all 0s (i.e., insert nop)
nop = sll $zero, $zero, 0

## Slide 23: RF Bypassing
Step 2b: Stall with register file bypassing
  Implement a write-before-read RF where the instruction at WB writes its result into the RF in the first half of the cycle and then the instruction at ID reads its operands.
  add $1, $2, $3
  sub $4, $5, $1
  lw $6, 0($7)
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
sub |  | F | D* | D* | D | X | M | W |  | 
lw |  |  | F* | F* | F | D | X | M | W | 

## Slide 24: Data Forwarding
Step 2c: RF bypassing and data forwarding
  For some instructions, their results are ready before WB
    Ready after EX for arithmetic and logic
  For all instructions, they do not need their operands until EX
  Add forwarding muxes to inputs of ALU
  Eliminates all stalls (except for load-to-use stalls, later)
  add $1, $2, $3
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  | 

## Slide 25: EX-to-EX Forwarding
  add $1, $2, $3
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  | 

## Slide 26: MEM-to-EX Forwarding
  add $1, $2, $3
  …
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
add | F | D | X | M | W |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  |  | 

## Slide 27: Load-to-Use Stalls
nop
  lw $1, 0($2)
  sub $4, $5, $1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
lw | F | D | X | M | W |  |  |  |  | 
sub |  | F | D* | D | X | M | W |  |  | 

## Slide 28: Data Forwarding
Actually not all operands are needed at EX stage
  Store instructions do not need RegisterRt until MEM stage
  MEM-to-MEM forwarding: implement in homework

## Slide 29: All Together

## Slide 30: Exercise
  lw $s1, 0($s2)
  lw $s3, 4($s1)
  add $s5, $s4, $s3
Assume full forwarding and bypassing:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 

## Slide 31: Exercise
  lw $s1, 0($s2)
  lw $s3, 4($s1)
  add $s5, $s4, $s3
Assume full forwarding and bypassing:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 32: Exercise
  lw $s1, 0($s2)
  lw $s3, 4($s1)
  add $s5, $s4, $s3
Assume full forwarding and bypassing:
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
stalls
NOP
NOP

## Slide 33: Exercise
lw $s3
add
lw $s1
cycle 3:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 34: Exercise
lw $s3
add
NOP
cycle 4:
lw $s1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 35: Exercise
lw $s3
add
NOP
cycle 5:
lw $s1
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 36: Exercise
lw $s3
add
NOP
cycle 6:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
NOP

## Slide 37: Exercise
lw $s3
add
cycle 7:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
NOP

## Slide 38: Exercise
add
cycle 8:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $s1 | F | D | X | M | W |  |  |  |  |  |  |  | 
 |  |  |  | X | M | W |  |  |  |  |  |  | 
lw $s3 |  | F | D* | D | X | M | W |  |  |  |  |  | 
 |  |  |  |  |  | X | M | W |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
NOP

## Slide 39: Exercise
MEM-to-EX forwarding
  But why not this instead?

## Slide 40: Exercise
MEM-to-EX forwarding
  But why not this instead? Critical path = MEM + EX delays