## Slide 1: ECE/CS 552: Control Hazards and Exceptions
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill and John Shen

## Slide 2: Announcements
Project Phase 1 Due October 21
  Follow all ISA rules carefully
  Follow submission rules carefully
    Use Vcheck!
    Create more programs if you wish, but test1-3 results are required
Midterm next week: Thursday 10/24 during class
  Midterm review in-class Wednesday 10/22

## Slide 3: Control Hazards
When an incorrect instruction is fetched because the outcome of a previous branch has not yet been resolved
  e.g., If branches resolved in M stage (COD Figure 4.51)

## Slide 4: Control Hazards
When an incorrect instruction is fetched because the outcome of a previous branch has not yet been resolved
  e.g., If branches resolved in M stage (COD Figure 4.51)
  beq $t0, $t1, TARGET
  lw $t3, 0($t0)
  add $t4, $t5, $t6
  or $t2, $t1, $t7
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | D | X | = |  |  |  |  |  |  |  | 
add |  |  | F | D | = |  |  |  |  |  |  |  | 
or |  |  |  | F | = |  |  |  |  |  |  |  | 
sub |  |  |  |  | F | D | X | M | W |  |  |  | 
  TARGET:
  sub $t5, $t0, $t5

## Slide 5: Control Hazards
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush, if taken: clear IF/ID.Instruction to 0 (inserts NOP to ID)
target
compare
flush instruction in IF

## Slide 6: Control Hazards
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D |  |  |  |  |  |  |  |  |  |  | 
lw |  | F |  |  |  |  |  |  |  |  |  |  | 
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X |  |  |  |  |  |  |  |  |  | 
lw |  | F | = |  |  |  |  |  |  |  |  |  | 
sub |  |  | F |  |  |  |  |  |  |  |  |  | 
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush, if taken: clear IF/ID.Instruction to 0 (inserts NOP to ID)
  beq $t0, $t1, TARGET
  lw $t3, 0($t0)
  add $t4, $t5, $t6
  or $t2, $t1, $t7
  TARGET:
  sub $t5, $t0, $t5

## Slide 7: Control Hazards
beq
lw
cycle 2:
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | = |  |  |  |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  |  |  |  |  | 
lw (NOP)
sub
beq
cycle 3:
lw (NOP)
sub
beq
cycle 4:
lw (NOP)
sub
beq
cycle 5:
lw (NOP)
sub
cycle 6:

## Slide 8: Control Hazards
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D |  |  |  |  |  |  |  |  |  |  | 
beq |  | F |  |  |  |  |  |  |  |  |  |  | 
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D | X | M | W |  |  |  |  |  |  |  | 
beq |  | F | D* | D* | D | X | M | W |  |  |  |  | 
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush, if taken: clear IF/ID.Instruction to 0 (inserts NOP to ID)
  But RAW hazards in ID stage?
    Stall (+ RF bypassing)
  add $t1, $t5, $t6
  beq $t0, $t1, TARGET

## Slide 9: Control Hazards
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush, if taken: clear IF/ID.Instruction to 0 (inserts NOP to ID)
target
compare
flush instruction in IF