## Slide 1: ECE/CS 552: Control Hazards and Exceptions
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill and John Shen

## Slide 2: Pipeline Hazards
Forecast:
  Program Control Dependences
  Pipeline Control Hazards
    Flushes
    Branch delay slots
    Branch prediction
  Exceptions

## Slide 3: Program Control Dependences
An instruction Y is control-dependent on an instruction X if the outcome of X determines whether or not Y will be executed
  Due to conditional branches:
    Branch must execute to determine which instruction to fetch next
    Instructions following a conditional branch are control-dependent on the branch instruction

## Slide 4: Program Control Dependence
e.g., List all control dependence:
  I0→I1, I0→I2
  I4→I0, I4→I1, I4→I2, I4→I3, I4→I4
I0: | bne | $s1, $s3, I3
I1: | add | $s0, $s1, $s4
I2: | sw | $s2, 4($s3)
I3: | lw | $s3, 0($s0)
I4: | beq | $s3, $s2, I0

## Slide 5: Program Control Dependences
Technically, control dependences need not be preserved
  Can execute instructions that should not have been executed, as long as program correctness is not affected:
    Data dependences are preserved
    No new exceptions incurred

## Slide 6: Pipeline Control Hazards
When an incorrect instruction is fetched because the outcome of a previous branch has not yet been resolved
  e.g., Assume branches resolved in M stage (COD Figure 4.51)

## Slide 7: Pipeline Control Hazards
When an incorrect instruction is fetched because the outcome of a previous branch has not yet been resolved
  e.g., Assume branches resolved in M stage (COD Figure 4.51)
  beq $t0, $t1, TARGET
  lw $t3, 0($t0)
  add $t4, $t5, $t6
  or $t2, $t1, $t7
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | D | X | M | W |  |  |  |  |  |  | 
add |  |  | F | D | X | M | W |  |  |  |  |  | 
or |  |  |  | F | D | X | M | W |  |  |  |  | 
sub |  |  |  |  | F | D | X | M | W |  |  |  | 
  TARGET:
  sub $t5, $t0, $t5

## Slide 8: Resolving Control Hazards
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | D | X | = |  |  |  |  |  |  |  | 
add |  |  | F | D | = |  |  |  |  |  |  |  | 
or |  |  |  | F | = |  |  |  |  |  |  |  | 
sub |  |  |  |  | F |  |  |  |  |  |  |  | 
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M |  |  |  |  |  |  |  |  | 
lw |  | F | D | X |  |  |  |  |  |  |  |  | 
add |  |  | F | D |  |  |  |  |  |  |  |  | 
or |  |  |  | F |  |  |  |  |  |  |  |  | 
Predict-not-taken:
  Fetch next insns speculatively; flush if branch is actually taken
  e.g., Assume branches resolved in M stage (COD Figure 4.51)
  beq $t0, $t1, TARGET
  lw $t3, 0($t0)
  add $t4, $t5, $t6
  or $t2, $t1, $t7
  TARGET:
  sub $t5, $t0, $t5

## Slide 9: Resolving Control Hazards
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush: clear IF/ID.Instruction to 0 (inserts NOP to ID)
target
compare
flush instruction in IF

## Slide 10: Resolving Control Hazards
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D |  |  |  |  |  |  |  |  |  |  | 
lw |  | F |  |  |  |  |  |  |  |  |  |  | 
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X |  |  |  |  |  |  |  |  |  | 
lw |  | F | = |  |  |  |  |  |  |  |  |  | 
sub |  |  | F |  |  |  |  |  |  |  |  |  | 
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush: clear IF/ID.Instruction to 0 (inserts NOP to ID)
  beq $t0, $t1, TARGET
  lw $t3, 0($t0)
  add $t4, $t5, $t6
  or $t2, $t1, $t7
  TARGET:
  sub $t5, $t0, $t5

## Slide 11: Resolving Control Hazards
beq
lw
cycle 2:
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | = |  |  |  |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  |  |  |  |  | 
lw (NOP)
sub
beq
cycle 3:
lw (NOP)
sub
beq
cycle 4:
lw (NOP)
sub
beq
cycle 5:
lw (NOP)
sub
cycle 6:

## Slide 12: Resolving Control Hazards
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D |  |  |  |  |  |  |  |  |  |  | 
beq |  | F |  |  |  |  |  |  |  |  |  |  | 
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
add | F | D | X | M | W |  |  |  |  |  |  |  | 
beq |  | F | D* | D | X | M | W |  |  |  |  |  | 
Predict-not-taken + resolve in ID:
  Compute target and compare in ID stage (COD Figure 4.65)
  Flush: clear IF/ID.Instruction to 0 (inserts NOP to ID)
  But RAW hazards in ID stage?
    Stall + EX-to-ID forwarding (and MEM-to-ID forwarding)
  add $t1, $t5, $t6
  beq $t0, $t1, TARGET

## Slide 13: Branch Delay Slots
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw | F | D | X | M | W |  |  |  |  |  |  |  | 
beq |  | F | D | X | M | W |  |  |  |  |  |  | 
add |  |  | F | D | X | M | W |  |  |  |  |  | 
sub |  |  |  | F | D | X | M | W |  |  |  |  | 
Branch delay slot:
  Instruction after branch always executed (avoids flush logic)
    Compiler is responsible for filling slot with legal instruction
  Assume branches resolved in ID stage (COD Figure 4.65)
  lw $t7, 0($t8)
  beq $t0, $t1, TARGET
  add $t5, $t4, $t6
  TARGET:
  sub $t5, $t0, $t5
not legal

## Slide 14: Branch Delay Slots
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw | F | D | X | M | W |  |  |  |  |  |  |  | 
beq |  | F | D | X | M | W |  |  |  |  |  |  | 
NOP |  |  | F | D | X | M | W |  |  |  |  |  | 
sub |  |  |  | F | D | X | M | W |  |  |  |  | 
Branch delay slot:
  Instruction after branch always executed (avoids flush logic)
    Compiler is responsible for filling slot with legal instruction
  Assume branches resolved in ID stage (COD Figure 4.65)
  lw $t7, 0($t8)
  beq $t0, $t1, TARGET
  sll $zero, $zero, 0
  add $t5, $t4, $t6
  TARGET:
  sub $t5, $t0, $t5
option 1:
insert NOP

## Slide 15: Branch Delay Slots
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
lw |  | F | D | X | M | W |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  |  |  |  |  | 
Branch delay slot:
  Instruction after branch always executed (avoids flush logic)
    Compiler is responsible for filling slot with legal instruction
  Assume branches resolved in ID stage (COD Figure 4.65)
  lw $t7, 0($t8)
  beq $t0, $t1, TARGET
  lw $t7, 0($t8)
  add $t5, $t4, $t6
  TARGET:
  sub $t5, $t0, $t5
option 2:
fill slot with existing instruction, if legal

## Slide 16: Branch Prediction
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
sub |  | F | D | X | M | W |  |  |  |  |  |  | 
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Assume branches resolved in ID stage (COD Figure 4.65)
  beq $t0, $t1, TARGET
  add $t5, $t4, $t6
  TARGET:
  sub $t5, $t0, $t5
predict taken
(correct)

## Slide 17: Branch Prediction
Cycle Instns | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
beq | F | D | X | M | W |  |  |  |  |  |  |  | 
add |  | F | = |  |  |  |  |  |  |  |  |  | 
sub |  |  | F | D | X | M | W |  |  |  |  |  | 
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Assume branches resolved in ID stage (COD Figure 4.65)
  beq $t0, $t1, TARGET
  add $t5, $t4, $t6
  TARGET:
  sub $t5, $t0, $t5
predict not taken
(incorrect)

## Slide 18: Branch Prediction
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Branch history table (BHT) with 1-bit prediction
BHT
N
T
T
N
T
N
N
T
0 Not Taken (N)
1 Taken (T)
Taken
Taken
Not Taken
Not Taken
PC[4:2]

## Slide 19: Branch Prediction
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Branch history table (BHT) with 1-bit prediction
  LOOP: …
  beq $t0, $t1, TARGET # predict
  …
  j LOOP
LOOP iteration | 1 | 2
prediction | N | T
outcome | T | T
LOOP iteration | 1
prediction | N
outcome | T
LOOP iteration | 1
prediction | N
LOOP iteration | 1 | 2 | 3 | 4 | 6 | 7 | 8 | 9
prediction | N | T | T | T | N | T | T | T
outcome | T | T | T | N | T | T | T | N
misprediction rate = 4/8

## Slide 20: Branch Prediction
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Branch history table (BHT) with 2-bit prediction
BHT
n
T
t
n
T
N
N
t
01 not taken (n)
00 Not Taken (N)
10 taken (t)
11 Taken (T)
Taken
Taken
Taken
Not Taken
Not Taken
Taken
Not Taken
Not Taken
PC[4:2]

## Slide 21: Branch Prediction
LOOP iteration | 1
prediction | n
outcome | T
LOOP iteration | 1
prediction | n
LOOP iteration | 1 | 2
prediction | n | t
outcome | T | T
Dynamic branch direction prediction:
  Predict branch outcome (T or N) in IF stage
  Target is either computed early or predicted too (advanced)
  Branch history table (BHT) with 2-bit prediction
  LOOP: …
  beq $t0, $t1, TARGET # predict
  …
  j LOOP
misprediction rate = 3/8
LOOP iteration | 1 | 2 | 3 | 4 | 6 | 7 | 8 | 9
prediction | n | t | T | T | t | T | T | T
outcome | T | T | T | N | T | T | T | N

## Slide 22: Exceptions
What happens?
  Arithmetic overflow
  Undefined opcode
  Instruction/data page fault
  I/O device status change
Invoke “surprise procedure call”
  Called an exception

## Slide 23: Exceptions
Two types:
  Interrupt (asynchronous)
  Trap (synchronous)
Hardware handles initial reaction
Then invokes a software exception handler
  Predefined (e.g., overflow handler: 0x80000180)
  OS kernel implements handler code

## Slide 24: Exceptions – Hardware
Record the cause of the exception
  MIPS 32-bit Cause register
Save current PC and flush pipeline
  MIPS 32-bit exception PC (EPC) register
Jump to exception handler
  e.g., Handler at address 0x80000180 for arithmetic overflow
  Like a surprise jump-and-link

## Slide 25: Exceptions – Hardware
e.g., Arithmetic overflow (COD Figure 4.66)
record Cause and EPC
flush EX
(and ID, IF)
jump to handler PC

## Slide 26: Exercise – Branch Prediction
Consider five-stage pipeline
  Assume accounting for data hazards, average CPI = 1.2
  Assume branches resolved in ID stage
  Assume 30% of instructions are branches: 60% are taken
  1) Predict-not-taken with 300us clock period?
    Average CPI = 1.2 + (1 × 30% × 60%) = 1.38
    1 / (1.38 × 300us) = 2415 instructions per sec
  2) 90%-accurate predictor with 325us clock period?
    Average CPI = 1.2 + (1 × 30% × 10%) = 1.23
    1 / (1.23 × 325us) = 2501 instructions per sec

## Slide 27: Exercise – Branch Delay Slot
  sub $s5, $s6, $s7
  nor $s1, $s2, $s3
  beq $s1, $s4, T1
  sll $0, $0, 0 # branch delay slot
  add $s4, $s5, $s6
  j T2
  …
  T1: or $s4, $s4, $s7
  slt $s2, $s4, $s6
  T2: and $s2, $s2, $s3
Ignore exceptions

## Slide 28: Exercise – Branch Delay Slot
  sub $s5, $s6, $s7
  nor $s1, $s2, $s3
  beq $s1, $s4, T1
  sub $s5, $s6, $s7 # branch delay slot – legal?
  add $s4, $s5, $s6
  j T2
  …
  T1: or $s4, $s4, $s7
  slt $s2, $s4, $s6
  T2: and $s2, $s2, $s3
yes
Ignore exceptions

## Slide 29: Exercise – Branch Delay Slot
  sub $s5, $s6, $s7
  nor $s1, $s2, $s3
  beq $s1, $s4, T1
  nor $s1, $s2, $s3 # branch delay slot – legal?
  add $s4, $s5, $s6
  j T2
  …
  T1: or $s4, $s4, $s7
  slt $s2, $s4, $s6
  T2: and $s2, $s2, $s3
no
Ignore exceptions

## Slide 30: Exercise – Branch Delay Slot
  sub $s5, $s6, $s7
  nor $s1, $s2, $s3
  beq $s1, $s4, T1
  add $s4, $s5, $s6 # branch delay slot – legal?
  add $s4, $s5, $s6
  j T2
  …
  T1: or $s4, $s4, $s7
  slt $s2, $s4, $s6
  T2: and $s2, $s2, $s3
no
Ignore exceptions

## Slide 31: Exercise – Branch Delay Slot
  sub $s5, $s6, $s7
  nor $s1, $s2, $s3
  beq $s1, $s4, T1
  or $s4, $s4, $s7 # branch delay slot – legal?
  add $s4, $s5, $s6
  j T2
  …
  T1: or $s4, $s4, $s7
  slt $s2, $s4, $s6
  T2: and $s2, $s2, $s3
yes
Ignore exceptions