## Slide 1: ECE/CS 552: Cache Concepts
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Announcements
Project Phase 1 Due October 21
  Follow all ISA rules carefully
  Follow submission rules carefully
    Use Vcheck!
    Create more programs if you wish, but test1-3 results are required
Midterm next week: Thursday 10/24 during class
  Midterm review in-class Wednesday 10/22
  Covers material through this class

## Slide 3: Memory Hierarchy
main memory (off-chip DRAM)
cache (on-chip SRAM)
Cache holds recently accessed multi-byte (e.g., 64B) blocks from memory for faster access
Leverages reuse
Cache miss, if not in cache, else hit
(1) lw $t0, 4000
(3) if not in cache, fetch (4000-4063)
from memory into cache
(2) cache lookup 4000
(4) [$t0] = (4000)

## Slide 4: Memory Hierarchy
main memory (off-chip DRAM)
cache (on-chip SRAM)
Cache holds recently accessed multi-byte (e.g., 64B) blocks from memory for faster access
Leverages reuse
Cache miss, if not in cache, else hit
(1) lw $t1, 4032
(2) cache lookup 4032, hit
(3) [$t1] = (4032)

## Slide 5: Caches – Placement
Memory address = { tag, index, block offset }
e.g., 256B cache capacity (can hold four 64B blocks)
data word
<<
=
6-bit offset
24-bit tag
2-bit index
hit?
data array
tag array
data block
e.g., 0x1000F348
0x08
0x1
(0x1000F340 – 0x1000F37F)
0x1000F3

## Slide 6: Caches – Replacement
(0x1000F340 – 0x1000F37F)
Memory address = { tag, index, block offset }
e.g., 256B cache capacity (can hold four 64B blocks)
data word
<<
=
6-bit offset
24-bit tag
2-bit index
hit?
data array
tag array
data block
e.g., 0xA060BB70
0x30
0x1
0x1000F3
MISS
(0xA060BB40 – 0xA060BB7F)
0xA060BB