## Slide 1: ECE/CS 552: Cache Performance
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Cache Hierarchy (e.g., 2-level)
L1-I cache
L1-D cache
unified I/D L2 cache
main memory

## Slide 3: Caches
Placement:
Where can a block of memory go?
Replacement:
How do we make space for new blocks?
Write Policy:
How do we propagate modifications to memory?

## Slide 4: Caches – Placement
Since memory address range exceeds cache capacity, map memory addresses into finite set of cache storage locations.
Set-associativity:
  Cache way: one possible storage location that a given block can be placed
  Cache set: group of ways for a given block
    N-way set-associative cache: every block has exactly N locations (ways) where it can be placed
    Direct-mapped cache: N = 1
    Fully-associative cache: N = total number of blocks in cache

## Slide 5: Caches – Placement
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | (X)
=
way 0
way N-1
way 0
way N-1
hit?
address X
data
tag
set
physical address
tag | set | offset
Standard hash function:
=
hit?
<<
block offset
hash function

## Slide 6: Caches – Placement
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | (X)
=
way 0
way N-1
way 0
way N-1
hit?
address X
data
tag
set
physical address
tag | set | offset
Standard hash function:
=
hit?
<<
block offset
hash function
e.g., Given 32-bit addresses and 64B blocks, what is the minimum number of tag bits needed in a 16-way associative 128KB cache?
(128KB / 64B per block) / 16 ways = 128 sets
32 bits – log(64B per block) – log(128 sets) = 19 tag bits

## Slide 7: Caches – Placement
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | (X)
=
way 0
way N-1
way 0
way N-1
hit?
address X
data
tag
set
physical address
tag | set | offset
Standard hash function:
=
hit?
<<
block offset
hash function
Hash function requirements:
1) A block must not be in multiple locations in the cache at once
2) A block must not be confused with a different block

## Slide 8: Caches – Replacement
Since cache capacity is finite, may need to evict a block in the cache to make space for another one.
Direct-mapped cache:
  Straightforward, evict current block at set index
Set-associative cache:
  Belady’s: Evict block that will be used furthest in future; unachievable optimum
  FIFO (first-in-first-out): Track age using simple timestamps
  LRU (least recently used): Maintain stack of last access; complex at high associativity
  NMRU (not most recently used): Just track the most recently used; randomly evict any of the other blocks

## Slide 9: Caches – Replacement
e.g., 32B 2-way associative cache:
  4B blocks, write-back, write-allocate, LRU
  6-bit memory addresses
  {2-bit tag, 2-bit set, 2-bit offset}
  Assume initially empty
Tag0 | Tag1 | LRU
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Load 0x3C | 111100 | 3 | Miss
Load 0x20 | 100000 | 0 | Miss
Load 0x33 | 110011 | 0 | Miss
Load 0x11 | 010001 | 0 | Miss, Evict
Store 0x29 | 101001 | 2 | Hit, Dirty
Tag Array (Binary)
10
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Load 0x3C | 111100 | 3 | Miss
Load 0x20 | 100000 | 0 | Miss
Load 0x33 | 110011 | 0 | Miss
Load 0x11 | 010001 | 0 | Miss, Evict
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Load 0x3C | 111100 | 3 | Miss
Load 0x20 | 100000 | 0 | Miss
Load 0x33 | 110011 | 0 | Miss
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Load 0x3C | 111100 | 3 | Miss
Load 0x20 | 100000 | 0 | Miss
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Load 0x3C | 111100 | 3 | Miss
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Load 0x2B | 101011 | 2 | Hit
Request | Binary | Set | Hit/Miss
Load 0x2A | 101010 | 2 | Miss
Request | Binary | Set | Hit/Miss
0
0
0
0
1
11
1
10
1
11
01
d

## Slide 10: Caches – Replacement
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | (X)
=
way 0
way N-1
way 0
way N-1
hit?
address X
data
tag
set
physical address
=
hit?
<<
block offset
hash function
if associativity is low, lots of cache thrashing

## Slide 11: Skewed-Associative Caches
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | (X)
=
way 0
way N-1
way 0
way N-1
hit?
address X
data
tag
=
hit?
<<
block offset
hash function
hash function
physical address
spreads out the likelihood of collisions
An analogy:
Tightly packed course schedule.
Discussion sessions for two courses collide at MWF 1pm-2:15pm.
With skewed schedule, courses get:
1) M 1pm, W 3pm, F 10am
2) M 1pm, W 11am, F 4pm

## Slide 12: Cache Performance
Cache miss rate:
Local: Percentage of accesses to cache that are misses (e.g., 10% miss rate)
  Local hit rate = 100% - local miss rate
Global: Misses per instruction (e.g., 1 MPKI = 1 miss per 1000 instructions)
  Or conversely, instructions per miss

## Slide 13: Cache Performance
Cache miss rate:
e.g., If one L1 miss per 30 instructions and the L1 local miss rate is 10%, what fraction of instructions in the program are a load or a store?
  1/30 = f × 1/10, thus f = 1/3
e.g., If one L1 miss per 20 instructions and one L2 miss per 80 instructions, what is the local miss rate of the L2 cache?
  1/80 = m × 1/20, thus m = 25%

## Slide 14: Cache Performance
Average memory access time (AMAT): Average time it takes (in cycles) between when the processor issues a request (to the cache/memory hierarchy) for an address and when it is received by the processor.
e.g., L1 cache with access latency tL1 (in cycles) and local miss rate %missL1:
  AMAT = tL1 + %missL1 × tMEM
  Usually, tL1 = 1 cycle
e.g., L1 cache + L2 cache:
  AMAT = tL1 + %missL1 × (tL2 + %missL2 × tMEM)
Apply recursively to N-level cache hierarchy:
  AMAT = tL1 + %missL1 × (tL2 + %missL2 × … (tLN + %missLN × tMEM))

## Slide 15: Cache Performance
e.g., Assume a 1-cycle L1 with 5% miss rate, a 10-cycle L2 with 20% miss rate and a 50-cycle main memory. How much higher is AMAT if we were to remove the L2?
AMAT, with L2 = 1 + 5% × (10 + 20% × 50) = 2 cycles
AMAT, without L2 = 1 + 5% × 50 = 3.5 cycles
  1.75x higher without the L2

## Slide 16: Cache Performance
What happens on a cache miss?
Stall, with five-stage pipeline
e.g., Assume pipelined processor (base CPI = 1) running program with 30% loads/stores:
A base CPI of 1 implies tL1 = 1 cycle
If L1-I miss rate is 2%, L1-D miss rate is 10%, and main memory delay is 10 cycles, what is average CPI?
  penaltyL1D = 30% × %missL1D × tMEM = 0.3 cycles per insn
  penaltyL1I = %missL1I × tMEM = 0.2 cycles per insn
  average CPI = CPIbase + penaltyL1I + penaltyL1D = 1.5

## Slide 17: Cache Misses
Compulsory (Cold) Miss:
Program’s first ever access to a given block of memory.
If infinite-size cache, every miss is a cold miss.
Capacity Miss:
Program’s memory footprint exceeds cache capacity.
If fully-associative finite cache, every miss that isn’t the first access (i.e., isn’t a cold miss) is a capacity miss.
Conflict Miss:
Placement restrictions cause useful blocks to be evicted.
Conflict misses only occur when a block can only be placed on a subset of the cache.

## Slide 18: Cache Misses
Vary capacity and associativity
  Compulsory misses are constant
  For fixed capacity, conflict misses ↓ as associativity ↑

## Slide 19: Cache Misses
Vary capacity and block size
  For fixed capacity, compulsory misses ↓ as block size ↑
  Capacity and conflict misses can increase with larger blocks

## Slide 20: Cache Misses
Reduce capacity misses?
Increase cache size
Increase program temporal locality
Reduce conflict misses?
Increase associativity
Improve replacement policy
Improve hash function
Reduce cold misses?
Increase block size
Increase program spatial locality
Implement prefetching

## Slide 21: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. How many cold misses?
int A[32768]; // base address 0x1000
for (int n = 0; n < 3; n++)
for (int i = 0; i < 32768; i++)
... = A[i];

## Slide 22: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. How many cold misses?
int A[32768]; // base address 0x1000
for (int n = 0; n < 3; n++)
for (int i = 0; i < 32768; i++)
... = A[i];
misses (n=0) | hits (n=0)
A[0] | A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15]
cold misses = 32768 / (64B / 4B per int) = 2048
misses (n=0) | hits (n=0)
A[0] | A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15]
A[16] | A[17] A[18] A[19] A[20] ... A[28] A[29] A[30] A[31]
A[32] | A[33] A[34] A[35] A[36] ... A[44] A[45] A[46] A[47]
... | ...

## Slide 23: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. How many capacity misses?
int A[32768]; // base address 0x1000
for (int n = 0; n < 3; n++)
for (int i = 0; i < 32768; i++)
... = A[i];

## Slide 24: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. How many capacity misses?
int A[32768]; // base address 0x1000
for (int n = 0; n < 3; n++)
for (int i = 0; i < 32768; i++)
... = A[i];
capacity misses = 2048 (when n=1) …
misses (n=1) | hits (n=1)
A[0] | A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15]
A[16] | A[17] A[18] A[19] A[20] ... A[28] A[29] A[30] A[31]
A[32] | A[33] A[34] A[35] A[36] ... A[44] A[45] A[46] A[47]
... | ...
capacity misses = 2048 (when n=1) + 2048 (when n=2)
misses (n=2) | hits (n=2)
A[0] | A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15]
A[16] | A[17] A[18] A[19] A[20] ... A[28] A[29] A[30] A[31]
A[32] | A[33] A[34] A[35] A[36] ... A[44] A[45] A[46] A[47]
... | ...

## Slide 25: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. How many total misses?
int A[32768]; // base address 0x1000
for (int n = 0; n < 3; n++)
for (int i = 0; i < 32768; i++)
... = A[i];
total misses = cold misses + capacity misses = 6144

## Slide 26: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. Now how many total misses?
int A[32768]; // base address 0x1000
for (int i = 0; i < 32768; i++)
for (int n = 0; n < 3; n++)
... = A[i];

## Slide 27: Exercise
Assume 4KB fully-associative data cache with 64B blocks and LRU replacement. Now how many total misses?
int A[32768]; // base address 0x1000
for (int i = 0; i < 32768; i++)
for (int n = 0; n < 3; n++)
... = A[i];
total misses = 3 × 32768 / (3 × 64B / 4B per int) = 2048
(in other words, eliminated capacity misses)
misses | hits
A[0] | A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15] A[0] A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15] A[0] A[1] A[2] A[3] A[4] A[5] A[6] A[7] A[8] A[9] A[10] A[11] A[12] A[13] A[14] A[15]
... | ...
improves temporal locality