## Slide 1: ECE/CS 552: Virtual Memory
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Virtual Memory
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
int main ()
{
// process A
}
int main ()
{
// process B
}
int main ()
{
// process C
}

## Slide 3: Virtual Memory
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
page table
int main ()
{
// process A
}
int main ()
{
// process B
}
int main ()
{
// process C
}
virtual
physical

## Slide 4: Page Tables
How are addresses translated? Software page walk
Each program is allocated a page table
  Managed by the OS
  Maps every VPN to a PPN
  Address translation = page table lookup (i.e., page walk)
Virtual Page Number (VPN)
Physical Page Number (PPN)
Page Offset
page table
virtual address
(e.g., 32-bit MIPS)
physical address
Page Offset

## Slide 5: Page Tables
int main ()
{
// process A
}
int main ()
{
// process B
}
virtual address space
virtual address space
physical memory
disk
page table
The page table itself is stored in physical memory

## Slide 6: Page Tables
Page table entry (PTE) contains:
  Physical page number
  Valid bit: specifies if page is in physical memory
    Upon a page walk, if invalid, page fault
  Dirty bit, permission bits, etc.
Page Table Entry
PTBR
Virtual Page Number
Offset
+
Page Table Base Register

## Slide 7: Multi-Level Page Tables
PPN
PTEs
base pointer
VPN
PPN
valid
valid
invalid
1st-level
pointers
2nd-level
PTEs
L2
L1
base pointer
VPN
VS.

## Slide 8: Virtual Memory
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
page table
int main ()
{
// process A
}
int main ()
{
// process B
}
int main ()
{
// process C
}
virtual
physical

## Slide 9: Virtual Memory
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
page table
TLB
TLB
int main ()
{
// process A
}
int main ()
{
// process B
}
int main ()
{
// process C
}
cache for page table entries
virtual
physical