## Slide 1: ECE/CS 552: Memory, ECC and I/O
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Address Translation
VA→PA mapping:
Split VA into virtual page number (VPN) and page offset (POFS)
Translate VPN into physical page number (PPN)
  POFS is not translated
  VA→PA = [VPN, POFS] → [PPN, POFS]
e.g.,
  64KB pages implies 16-bit POFS
  32-bit machine implies 32-bit VA; thus 16-bit VPN
  Maximum 256MB physical memory implies 28-bit PA; thus 12-bit PPN
[15:0] = POFS
virtual address[31:0]
[31:16] = VPN
[15:0] = POFS
physical address[27:0]
[27:16] = PPN
translate
don’t touch

## Slide 3: Physical (PIPT) Cache
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
page table
TLB
TLB
virtual
physical

## Slide 4: Virt-Indexed Phys-Tagged (VIPT) Cache
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
page table
TLB
TLB
virtual
physical

## Slide 5: VIPT Cache
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
physical address
virtual address
cache indexing in parallel to TLB lookup
Synonyms: different virtual address → same physical address?
TLB

## Slide 6: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VA
physical address
virtual address
TLB

## Slide 7: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | [X]
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VA
VA -> X
physical address
virtual address
TLB

## Slide 8: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | [X]
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VB
physical address
virtual address
TLB

## Slide 9: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | [X]
X |  |  |  | [X] |  | 
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VB
VB -> X
synonym problem:
two copies of same physical block!
physical address
virtual address
TLB

## Slide 10: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | [X]
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VA, VB
solution:
map VA and VB to the same set
physical address
virtual address
TLB

## Slide 11: VIPT Cache – Synonyms
tag |  | tag |  | data |  | data
 | ● ● ● |  |  |  | ● ● ● | 
 |  | X |  |  |  | [X]
=
way 0
way N-1
way 0
way N-1
HIT?
hash function
data
tag
set
VA,VB -> X
VA, VB
solution:
map VA and VB to the same set
But don’t know VA and VB a priori; how to map them to the same set?
physical address
virtual address
TLB

## Slide 12: VIPT Cache – Synonyms
e.g., Assume 4KB pages. If the physical address of our data is 0x1A318ED4, and virtual addresses VA and VB both map to it, what do we know about VA and VB?
VA = 0x______ED4
VB = 0x______ED4
So then without knowing what VA and VB exactly are, how can we make sure they always map to the same set in our VIPT cache?

## Slide 13: Error Correction Codes
Main memory stores a huge number of bits
  Probability of bit-flip becomes significant
  Bit-flips (called soft errors) caused by
    Gamma rays and alpha particles
    Electrical interference
    etc.
  Getting worse with smaller feature sizes
Systems must be protected from soft errors via error correction codes (ECC)

## Slide 14: Exercise – ECC