## Slide 1: ECE/CS 552: Memory, ECC and I/O
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Main Memory
Commodity DRAM chips
Design objectives:
  Minimizing cost, latency
  Maximizing bandwidth, capacity
Susceptible to soft errors
  Protect with error correction codes (ECC)
  ECC also widely used in on-chip memories/buses

## Slide 3: Main Memory – DRAM
Data stored as charge in capacitor
Discharge on reads
Charge leaks over time
  Refresh periodically
  e.g., Every 64ms
Read entire row to row buffer
  Row address strobe (RAS), page open
Read word from row buffer
  Column address strobe (CAS)
Write row back
  Precharge, page close

## Slide 4: Main Memory – Access
e.g., Main memory access for 4-word cache block:
Note that DRAM bus cycles are ~10x CPU cycle time
1) Read entire row into row buffer (RAS, page open)
  5 cycles to send row address and read row
2) Read each word from row buffer (CAS)
  1 cycle to send column address
  3 cycle DRAM internal access delay
  1 cycle to receive data word on bus
3) Precharge (page close)
  5 cycles to precharge

## Slide 5: Main Memory – Access
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
one-word-wide bus

## Slide 6: Main Memory – Access
e.g., One word wide:
  r=row addr, c=col addr, d=DRAM delay, b=bus, p=precharge
  rrrrrcdddbcdddbcdddbcdddbppppp
  5 + 4 * (1 + 3 + 1) = 25 cycles to fetch data
  (then 5 cycles until next access allowed)
e.g., One word wide, burst mode (pipelined):
  rrrrrcdddb
  b
  b
  bppppp
  5 + 1 + 3 + 4 = 13 cycles (then 5 cycles until next access)

## Slide 7: Main Memory – Access
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
four-word-wide bus

## Slide 8: Main Memory – Access
e.g., Four word wide:
  rrrrrcdddbppppp
  5 + 1 + 3 + 1 = 9 cycles (then 5 cycles until next access)

## Slide 9: ECC
Main memory stores a huge number of bits
  Probability of bit-flip becomes significant
  Bit-flips (called soft errors) caused by
    Gamma rays and alpha particles
    Electrical interference
    etc.
  Getting worse with smaller feature sizes
Systems must be protected from soft errors via error correction codes (ECC)

## Slide 10: ECC
Probability of bit errors in a single word:
  P(0 errors) > P(1 error) > P(2 errors) >> P(>2 errors)
Detection: signal a problem
Correction: restore data to correct value

## Slide 11: No ECC
Data Word (1 bit) | Codeword in Memory (1 bit)
0 | 0
1 | 1
A single bit of data is stored as one bit in memory
Hamming Distance: how many bits must flip to convert a valid codeword to a different valid codeword?
Hamming Distance = 1

## Slide 12: Single Error Detection (SED)
Data Word (1 bit) | Codeword in Memory (2 bits)
0 | 00
1 | 11
Store one extra bit of redundancy in memory
Hamming Distance = 2
01
10
11
00
each edge is one bit-flip
01
if we observe invalid codeword, which bit flipped?

## Slide 13: Single Error Correction (SECSED)
Data Word (1 bit) | Codeword in Memory (3 bits)
0 | 000
1 | 111
Store two extra bits of redundancy in memory
Hamming Distance = 3
001
010
011
100
101
110
111
000
101
if we observe invalid codeword, assuming only one bit flipped, we know exactly which valid codeword we had previously

## Slide 14: SED – Parity
Data Word (4 bits) | Codeword in Memory (4 bits + 1 parity bit)
0000 | 00000
0001 | 00011
0010 | 00101
0011 | 00110
0100 | 01001
0101 | 01010
For arbitrary n-bit data word (bn…b1), add one parity bit P to codeword
Hamming Distance = 2
P = b1 ⊕ … ⊕ bn
When reading codeword, check syndrome = P⊕b1⊕…⊕bn== 0?
Note: following discussions assume one-based indexing

## Slide 15: SECSED – Hamming Code
For arbitrary n-bit data word (bn…b1), add k check bits (Ck…C1) to codeword, where 2k ≥ n+k+1
e.g., Hamming(7,4): n=4, k=3; Hamming Distance = 3

## Slide 16: SECSED – Hamming(7,4)
Store a 4-bit data word (b4b3b2b1) as a 7-bit codeword (W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 3-bit syndrome (S3S2S1) that specifies if any (and which) bit has flipped:
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7

## Slide 17: SECSED – Hamming(7,4)
Store a 4-bit data word (b4b3b2b1) as a 7-bit codeword (W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 3-bit syndrome (S3S2S1) that specifies if any (and which) bit has flipped:
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Syndrome | 
S1 | 
S2 | 
S3 | 
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | 
S3 | 
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | 
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7

## Slide 18: SECSED – Hamming(7,4)
Store a 4-bit data word (b4b3b2b1) as a 7-bit codeword (W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 3-bit syndrome (S3S2S1) that specifies if any (and which) bit has flipped:
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
e.g., if both S1 and S3 are 1,
then W5 must have flipped
e.g., S1 is 1 if any one of W1, W3, W5 or W7 flipped

## Slide 19: SECSED – Hamming(7,4)
Store a 4-bit data word (b4b3b2b1) as a 7-bit codeword (W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 3-bit syndrome (S3S2S1) that specifies if any (and which) bit has flipped:
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Codeword | 
W1 | 
W2 | 
W3 | 
W4 | 
W5 | 
W6 | 
W7 | 
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Codeword | 
W1 | C1=W3⊕W5⊕W7
W2 | C2=W3⊕W6⊕W7
W3 | 
W4 | C3=W5⊕W6⊕W7
W5 | 
W6 | 
W7 | 
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
use these as check bits (i.e., parity)
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Codeword | 
W1 | C1=W3⊕W5⊕W7
W2 | C2=W3⊕W6⊕W7
W3 | b1
W4 | C3=W5⊕W6⊕W7
W5 | b2
W6 | b3
W7 | b4
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
Syndrome | Bit flipped?
000 | none
001 | W1
010 | W2
011 | W3
100 | W4
101 | W5
110 | W6
111 | W7
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
Syndrome | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7

## Slide 20: SECDED – Hamming(7,4) + Parity
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Store a 4-bit data word (b4b3b2b1) as an 8-bit codeword (W8W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 4-bit syndrome that includes a 1-bit parity (S3S2S1, SP):
Hamming Distance = 4

## Slide 21: SECDED – Hamming(7,4) + Parity
Store a 4-bit data word (b4b3b2b1) as an 8-bit codeword (W8W7W6W5W4W3W2W1) in memory. Whenever we read the codeword, generate a 4-bit syndrome that includes a 1-bit parity (S3S2S1, SP):
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | 
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | 
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
use this as parity bit of entire codeword

## Slide 22: SECDED – Hamming(7,4) + Parity
e.g., Encode b4b3b2b1 = 0101 into an 8-bit codeword:
W8W7W6W5W4W3W2W1 = ____________
e.g., Encode b4b3b2b1 = 0101 into an 8-bit codeword:
W8W7W6W5W4W3W2W1 = 00101101
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1

## Slide 23: SECDED – Hamming(7,4) + Parity
Compare this to simply storing the bits redundantly:
Hamming(7,4) + Parity (SECDED Codeword) | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
1-Bit Redundancy (SED Codeword) | 
W1 | b1
W2 | b2
W3 | b3
W4 | b4
W5 | b1
W6 | b2
W7 | b3
W8 | b4
vs.

## Slide 24: Input/Output
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
I/O
I/O
I/O
I/O necessary:
  To/from users (display, keyboard, mouse)
  To/from non-volatile media (disk)
  To/from other computers (networks)

## Slide 25: Disk
Stack of platters:
  Two surfaces per platter
  Multiple tracks per surface
    Surface head moves to select track
    Heads of all platters synchronized
  Multiple sectors per track
    Platters rotate to select sector

## Slide 26: Disk – RAID
Redundant arrays of inexpensive disks (RAID):
  Handles disk failures
  e.g., Given a 100-disk system, if mean time to failure per disk is 5 years: over a long period of time, 1 disk fails every 18 days
Unlike memory ECC, we can tell when (and which) disks fail via diagnostics
  Just need to be able to recover the data

## Slide 27: Disk – RAID
RAID 0:
  Block-level striping
  No failure protection
RAID 1:
  Block-level striping
  Store all data twice (mirroring)
RAID 3:
  Bit-interleaved parity
disk0 | disk1 | disk2
block0 | block1 | block2
block3 | block4 | block5
block6 | block7 | block8
block9 | block10 | block11
disk0 | disk1 | disk2 | disk3
bit0 | bit1 | bit2 | parity0-2
bit3 | bit4 | bit5 | parity3-5
bit6 | bit7 | bit8 | parity6-8
bit9 | bit10 | bit11 | parity9-11

## Slide 28: Disk – RAID
RAID 4:
  Block-interleaved parity
RAID 5:
  Distributed block-interleaved parity
disk0 | disk1 | disk2 | disk3
block0 | block1 | block2 | parity0-2
block3 | block4 | block5 | parity3-5
block6 | block7 | block8 | parity6-8
block9 | block10 | block11 | parity9-11
disk0 | disk1 | disk2 | disk3
block0 | block1 | block2 | parity0-2
block3 | block4 | parity3-5 | block5
block6 | parity6-8 | block7 | block8
parity9-11 | block9 | block10 | block11

## Slide 29: Input/Output
How to communicate from host processor to I/O device?
  Memory-mapped I/O vs. ISA commands for I/O
virtual address space
memory-mapped I/O register
instruction set
read/write I/O register

## Slide 30: Input/Output
How to communicate from I/O device to host processor?
  Polling vs. interrupts
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
I/O
I/O
I/O
poll (read) I/O register
interrupt processor
(similar to exceptions)

## Slide 31: Buses

## Slide 32: Buses
Bunch of wires:
  Arbitration
  Control
  Data
  Address

## Slide 33: Buses
Synchronous bus: has clock
  Everyone watches clock and latches at appropriate phase
  Transactions take fixed or variable number of cycles
  Faster but clock limits bus length
  e.g., Processor-memory
Asynchronous bus: requires handshake
  More flexible
  e.g., I/O

## Slide 34: Buses – Asynchronous
(1) Request sent
(3) Request deasserted
(6) Data response received
Req/Data
(2) Request received
(4) Ack deasserted
(5) Data response sent
(7) Data response deasserted

## Slide 35: Input/Output – Caches
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
I/O
I/O
I/O
slows down loads/stores

## Slide 36: Input/Output – Caches
L1-I cache
L1-D cache
unified I/D L2 cache
main memory
I/O
I/O
I/O
no access to up-to-date data in caches

## Slide 37: Exercise – SECDED
e.g., A single bit-flip has occurred. Recover original data:
W8W7W6W5W4W3W2W1 = 00101001
b4b3b2b1 = __________
e.g., A single bit-flip has occurred. Recover original data:
W8W7W6W5W4W3W2W1 = 00101001
b4b3b2b1 = __________
e.g., A single bit-flip has occurred. Recover original data:
W8W7W6W5W4W3W2W1 = 00101001
b4b3b2b1 = 0101
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | 1
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | 1
S2 | 1
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | 1
S2 | 1
S3 | 0
SP | W8⊕…⊕W1
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
Syndrome, Parity | 
S1 | 1
S2 | 1
S3 | 0
SP | 1