## Slide 1: ECE/CS 552: Superscalar and Out-of-Order
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Out-of-Order Execution
High-level concept:
Fetch and decode in-order into instruction buffer
Insns check ready bits of their operands every cycle
  Dynamically schedule instructions out-of-order for execution while maintaining data dependences
  Only look at register dependences (ignore mem)
regfile
D$
I$
B
P
insn buffer

## Slide 3: Scoreboard
Scoreboard: allow instructions to bypass each other with two new stages:
Dispatch (Di): in-order stage
  Allocate slot in scoreboard (i.e., instruction buffer)
  Stall propagates to all younger instructions
Issue (S): out-of-order stage
  Select instruction from scoreboard to execute when operands ready
  Wait doesn’t propagate to all younger instructions
regfile
D$
I$
B
P
scoreboard
S
Di

## Slide 4: Register Renaming
Now that instructions execute out-of-order, WAR and WAW dependences become hazards too!
addi $t0, $t0, 4
lw $t1, 0($s0) # cache miss!
add $s1, $t1, $s2
or $t1, $t0, $s0 # not dependent on lw
sub $t1, $t1, $s2 # not dependent on lw
bne $s1, $t1, TARGET

## Slide 5: Register Renaming
Now that instructions execute out-of-order, WAR and WAW dependences become hazards too!
addi $t0, $t0, 4
or $t1, $t0, $s0 # not dependent on lw
sub $t1, $t1, $s2 # not dependent on lw
lw $t1, 0($s0) # cache miss!
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET # wrong value of [$t1]!

## Slide 6: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4
lw $t1, 0($s0)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1
$t1 | P3
$s0 | P6
$s1 | P2
$s2 | P0
free list
P5, P8, P4, P7, P9

## Slide 7: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1 P5
$t1 | P3
$s0 | P6
$s1 | P2
$s2 | P0
free list
P8, P4, P7, P9

## Slide 8: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) lw P8, 0(P6)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1 P5
$t1 | P3 P8
$s0 | P6
$s1 | P2
$s2 | P0
free list
P4, P7, P9

## Slide 9: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) lw P8, 0(P6)
add $s1, $t1, $s2 add P4, P8, P0
or $t1, $t0, $s0 or P7, P5, P6
sub $t1, $t1, $s2 sub P9, P7, P0
bne $s1, $t1, TARGET bne P4, P9, TARGET
map table | 
$t0 | P1 P5
$t1 | P3 P8 P7 P9
$s0 | P6
$s1 | P2 P4
$s2 | P0
free list
-