## Slide 1: ECE/CS 552: Superscalar and Out-of-Order
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Limitations of Scalar Pipelines
Upper bound on throughput
  IPC <= 1 (or CPI >= 1)
  Solution: enable more than one instruction to be executed in a cycle (i.e., superscalar)
Inefficient unified pipeline
  Varying latencies of instructions
  Solution: enable diversified, specialized pipelines
Rigid pipeline stall policy
  One stalled instruction stalls all newer instructions
  Solution: enable independent instructions to bypass each other (i.e., out-of-order execution)

## Slide 3: Superscalar Processors
Superscalar: more than one instruction can be executed in a cycle
  Static multiple-issue: parallel pipeline lanes
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
I1 | F | D | X | M | W |  |  | 
I2 | F | D | X | M | W |  |  | 
I3 |  | F | D | X | M | W |  | 
I4 |  | F | D | X | M | W |  | 

## Slide 4: Superscalar Processors
Superscalar: more than one instruction can be executed in a cycle
  Static multiple-issue: parallel pipeline lanes
    e.g., 1 lane for ALU/branch, 1 lane for load/store

## Slide 5: Superscalar Processors
Superscalar: more than one instruction can be executed in a cycle
  Out-of-order (OoO): instructions that are not dependent on each other can bypass each other
out-of-order
in-order
in-order

## Slide 6: Superscalar Processors
Step-by-step topics:
Scoreboard:
  Dynamic scheduling for enabling OoO execution
MIPS R10K:
  Register renaming for eliminating WAR/WAW hazards
  Reorder buffer for handling speculation/precise state

## Slide 7: In-Order Execution
e.g., What’s happening in cycle 4?
RAW hazard: lw misses -> add stalls
  OK, this is a fundamental problem
Structural hazard: propagated stall for sub
  Can’t proceed through pipeline due to stalled instruction in front of it, even though no data dependence
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
lw $t2,0($t0) | F | D | X | M | M | M | M | W |  |  | 
add $t2,$t3,$t2 |  | F | D* | D* | D* | D* | D* | X | M | W | 
sub $t4,$t1,$t0 |  |  | F* | F* | F* | F* | F* | D | X | M | W

## Slide 8: Out-of-Order Execution
High-level concept:
Fetch and decode in-order into instruction buffer
Insns check ready bits of their operands every cycle
  Dynamically schedule instructions out-of-order for execution while maintaining data dependences
  Only look at register dependences (ignore mem)
regfile
D$
I$
B
P
insn buffer

## Slide 9: Out-of-Order Execution
Insns check ready bits of their operands every cycle
  Dynamically schedule instructions out-of-order for execution while maintaining data dependences
  Only look at register dependences (ignore mem)
add $t4,$t3,$t2
sub $t5,$t4,$t2
or $t6,$t5,$t2
addi $t7,$t4,4
Ready Table |  |  |  |  | 
$t2 | $t3 | $t4 | $t5 | $t6 | $t7
Yes | Yes |  |  |  | 
Yes | Yes | Yes |  |  | 
Yes | Yes | Yes | Yes |  | Yes
Yes | Yes | Yes | Yes | Yes | Yes
addi $t7,$t4,4
or $t6,$t5,$t2
sub $t5,$t4,$t2
add $t4,$t3,$t2
and
time

## Slide 10: Out-of-Order Execution
Instruction scheduling:
Goal: rearrange instructions to enable rapid issue
  Issue: time at which instructions execute
  Schedule: order in which instructions execute
  Requires knowledge of pipeline and program dependences
  Requires large scheduling scope full of independent instructions
Static scheduling: compiler
Dynamic scheduling: OoO hardware

## Slide 11: Scoreboard
Scoreboard: allow instructions to bypass each other with two new stages:
Dispatch (Di): in-order stage
  Allocate slot in scoreboard (i.e., instruction buffer)
  Stall propagates to all younger instructions
Issue (S): out-of-order stage
  Select instruction from scoreboard to execute when operands ready
  Wait doesn’t propagate to all younger instructions
regfile
D$
I$
B
P
scoreboard
S
Di

## Slide 12: Scoreboard
regfile
D$
I$
B
P
scoreboard
S
Di
F-regfile
FP/
FP
+
FP
+
FP*
FP*
FP*
out-of-order
in-order

## Slide 13: Scoreboard
Fetch (F) and Decode (De):
  Same as before
Dispatch (Di):
  Structural hazard or WAW hazard ? stall until older insn’s W
  Else: allocate scoreboard entry (per functional unit)
Issue (S):
  RAW hazard ? wait : read registers, go to functional unit
Execute (X):
  Execute ALU/branch/mem op
Writeback (W):
  WAR hazard ? wait until after older insn’s S
  Else: write register, notify readers and free scoreboard entry
  Assume RF bypassing from W to S in same cycle
out-of-order
in-order

## Slide 14: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw |  |  | 
sw |  |  | 
sub |  |  | 
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 15: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw | lw $t0, 0($s0) | $s0+ | 
sw |  |  | 
sub |  |  | 
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 16: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw |  |  | 
sub |  |  | 
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 17: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S |  |  |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di |  |  |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw | sw $t1, 4($s1) | $s1+ | $t1+
sub |  |  | 
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 18: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S |  |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S |  |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De |  |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw | sw $t1, 4($s1) | $s1+ | $t1+
sub | sub $t1, $s1, $s2 | $s1+ | $s2+
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 19: Scoreboard
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S |  |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X |  |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S |  |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di |  |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw | sw $t1, 4($s1) | $s1+ | $t1+
sub | sub $t1, $s1, $s2 | $s1+ | $s2+
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
assume 5 cycles to execute lw, else 1 cycle

## Slide 20: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S |  |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X |  |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di |  |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw |  |  | 
sub | sub $t1, $s1, $s2 | $s1+ | $s2+
assume 5 cycles to execute lw, else 1 cycle

## Slide 21: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X | X |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | S |  |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di | Di |  |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De | De |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | $t0- | $s1+
lw | lw $t0, 0($s0) | $s0+ | 
sw |  |  | 
sub | sub $t1, $s1, $s2 | $s1+ | $s2+
assume 5 cycles to execute lw, else 1 cycle

## Slide 22: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X | X | W |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | S | S |  |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X | W | W |  |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di | Di | Di |  |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De | De | De |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi | addi $t0, $t3, 16 | $t3+ | 
bne | bne $t0, $s1, DEST | $t0+ | $s1+
lw |  |  | 
sw |  |  | 
sub | sub $t1, $s1, $s2 | $s1+ | $s2+
assume 5 cycles to execute lw, else 1 cycle

## Slide 23: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X | X | W |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | S | S | X |  |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X | W | W | W |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di | Di | Di | S |  |  |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De | De | De | Di |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi | addi $t0, $t3, 16 | $t3+ | 
bne | bne $t0, $s1, DEST | $t0+ | $s1+
lw |  |  | 
sw | sw $t4, 0($s4) | $s4+ | $t4+
sub |  |  | 
assume 5 cycles to execute lw, else 1 cycle

## Slide 24: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X | X | W |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | S | S | X | W |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X | W | W | W |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di | Di | Di | S | X | W |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De | De | De | Di | S | X | W |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw |  |  | 
sw |  |  | 
sub |  |  | 
assume 5 cycles to execute lw, else 1 cycle
lots of stalling for WAW hazard
lots of waiting for WAR hazard

## Slide 25: Scoreboard
assume predict-not-taken, branches resolved in X
+ means register ready, - means not ready
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | X | X | W |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | S | S | X | W |  |  |  |  | 
sw $t1, 4($s1) |  |  | F | De | Di | S | X | W |  |  |  |  |  |  |  |  | 
sub $s1, $s1, $s2 |  |  |  | F | De | Di | S | X | W | W | W |  |  |  |  |  | 
addi $t0, $t3, 16 |  |  |  |  | F | De | Di | Di | Di | Di | S | X | W |  |  |  | 
sw $t4, 0($s4) |  |  |  |  |  | F | De | De | De | De | Di | S | X | W |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
scoreboard |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw |  |  | 
sw |  |  | 
sub |  |  | 
assume 5 cycles to execute lw, else 1 cycle
…but store instruction already modified memory!
what if branch taken? resolved at X…

## Slide 26: Superscalar Processors
Step-by-step topics:
Scoreboard:
  Dynamic scheduling for enabling OoO execution
MIPS R10K:
  Register renaming for eliminating WAR/WAW hazards
  Reorder buffer for handling speculation/precise state

## Slide 27: Register Renaming
Now that instructions execute out-of-order, WAR and WAW dependences become hazards too!
addi $t0, $t0, 4
lw $t1, 0($s0) # cache miss!
add $s1, $t1, $s2
or $t1, $t0, $s0 # not dependent on lw
sub $t1, $t1, $s2 # not dependent on lw
bne $s1, $t1, TARGET

## Slide 28: Register Renaming
Now that instructions execute out-of-order, WAR and WAW dependences become hazards too!
addi $t0, $t0, 4
or $t1, $t0, $s0 # not dependent on lw
sub $t1, $t1, $s2 # not dependent on lw
lw $t1, 0($s0) # cache miss!
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET # wrong value of [$t1]!

## Slide 29: Register Renaming
Change register names to eliminate WAR/WAW hazards
Key: think of ISA registers ($t1, $s0, …) as names not storage locations
  Can have more locations than names
  Can have multiple active versions of same name
Map table: maps names (architectural registers) to most recent storage locations (physical registers)
Free list: tracks which physical registers currently do not map to any architectural register
For each src arch reg: find physical reg of most recent write by consulting map table
For dest arch reg: allocate new physical reg, record in map table
Upon writeback: deallocate old physical reg back into free list

## Slide 30: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4
lw $t1, 0($s0)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1
$t1 | P3
$s0 | P6
$s1 | P2
$s2 | P0
free list
P5, P8, P4, P7, P9

## Slide 31: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1 P5
$t1 | P3
$s0 | P6
$s1 | P2
$s2 | P0
free list
P8, P4, P7, P9

## Slide 32: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) lw P8, 0(P6)
add $s1, $t1, $s2
or $t1, $t0, $s0
sub $t1, $t1, $s2
bne $s1, $t1, TARGET
map table | 
$t0 | P1 P5
$t1 | P3 P8
$s0 | P6
$s1 | P2
$s2 | P0
free list
P4, P7, P9

## Slide 33: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) lw P8, 0(P6)
add $s1, $t1, $s2 add P4, P8, P0
or $t1, $t0, $s0 or P7, P5, P6
sub $t1, $t1, $s2 sub P9, P7, P0
bne $s1, $t1, TARGET bne P4, P9, TARGET
map table | 
$t0 | P1 P5
$t1 | P3 P8 P7 P9
$s0 | P6
$s1 | P2 P4
$s2 | P0
free list
-

## Slide 34: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) or P7, P5, P6
add $s1, $t1, $s2 sub P9, P7, P0
or $t1, $t0, $s0 lw P8, 0(P6) # cache miss
sub $t1, $t1, $s2 add P4, P8, P0
bne $s1, $t1, TARGET bne P4, P9, TARGET
map table | 
$t0 | P1 P5
$t1 | P3 P8 P7 P9
$s0 | P6
$s1 | P2 P4
$s2 | P0
free list
-
can execute out-of-order
while preserving dependences!

## Slide 35: Exercise – Register Renaming
Dynamically map architectural regs to physical regs:
addi $t0, $t0, 4 addi P5, P1, 4
lw $t1, 0($s0) lw P8, 0(P6)
add $s1, $t1, $s2 add P4, P8, P0
or $t1, $t0, $s0 or P7, P5, P6
sub $t1, $t1, $s2 sub P9, P7, P0
bne $s1, $t1, TARGET bne P4, P9, TARGET
map table | 
$t0 | P5
$t1 | P9
$s0 | P6
$s1 | P4
$s2 | P0
free list
P1, P3, P2, P8, P7
…but need to writeback in-order

## Slide 36: Speculation
Execution of instructions before confirming that they need to be executed or before confirming that their operands are correct
  e.g., Branch prediction yields speculation of subsequent instructions in the predicted control path
  e.g., Memory dependence prediction yields speculation of load insns that come after a store insn whose address is not yet known
  e.g., Value prediction yields speculation of subsequent instructions that read the predicted value
Need to maintain precise state upon misspeculation:
  Revert processor as if younger instructions never executed
  Same procedure for exceptions and interrupts