## Slide 1: ECE/CS 552: MIPS R10K
Boone Severson
Lecture notes based on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Superscalar Processors
Step-by-step topics:
Scoreboard:
  Dynamic scheduling for enabling OoO execution
MIPS R10K:
  Register renaming for eliminating WAR/WAW hazards
  Reorder buffer for handling speculation/precise state

## Slide 3: Scoreboard
Problem: writeback stage combines two distinct operations:
Propagates result to younger instructions
  Ok to be out-of-order
Writes result to register file
  Would like this to be in-order
regfile
D$
I$
B
P
scoreboard

## Slide 4: MIPS R10K
Reorder buffer (ROB): buffers completed results en route to registers. Split writeback into 2 stages:
Complete (C): out-of-order
  After execution, instructions write results into ROB
Retire (R): in-order
  ROB writes results into register file
regfile
D$
I$
B
P
reorder buffer (ROB)
C
R

## Slide 5: MIPS R10K
Register renaming: Removes WAR/WAW hazards by holding multiple versions of architectural registers
Architectural register file? Gone
Physical register file holds all values:
  # physical registers = # architectural registers + # ROB entries
Map table maps architectural registers to most recent physical registers
Free list keeps track of unallocated physical registers

## Slide 6: MIPS R10K
When to free physical registers?
When an instruction retires:
  Can’t free physical register currently mapped to destination architectural register
  Can free physical register previously mapped to destination architectural register
    Why? All instructions that will ever read the previous value must have already retired (because we’re overwriting it)

## Slide 7: MIPS R10K – Pipeline
MIPS R10K-like processor:
Scalar in-order front-end
  F, De, Di
Branches are resolved at X stage and immediately flush the pipeline if mispredicted
Each reservation station is bound to a functional unit

## Slide 8: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P5 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P1, P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2

## Slide 9: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De |  |  |  |  |  |  | 
map table |  | 
$t0 | P5 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P1, P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Fetch (F):
  Get instruction from memory
  Update PC
Decode (De):
  Determine operation and operands

## Slide 10: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De | Di |  |  |  |  |  | 
map table |  | 
$t0 | P5 P1 | !rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P1, P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add | add $t0, $s1, $s2 | P4+ | P0+
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
add $t0, $s1, $s2 | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Dispatch (Di):
  Stall if no available reservation station, reorder buffer full, or no free physical register
  Determine which physical registers contain operands and allocate reservation station
  Allocate new physical register for output result and remember old register
  Allocate reorder buffer entry

## Slide 11: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De | Di | S |  |  |  |  | 
map table |  | 
$t0 | P1 | !rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add | add $t0, $s1, $s2 | P4+ | P0+
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
add $t0, $s1, $s2 | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Issue (S):
  Wait if operands are not ready yet or if no available functional unit
  Allocate functional unit, then free reservation station

## Slide 12: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De | Di | S | X |  |  |  | 
map table |  | 
$t0 | P1 | !rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
add $t0, $s1, $s2 | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Execute (X):
  Perform operation

## Slide 13: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De | Di | S | X | C |  |  | 
map table |  | 
$t0 | P1 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
add |  |  | 
bne | … | P1+ | 
lw* |  |  | 
sub | … |  | P1+
reorder buffer |  | 
insn | rd | old
add $t0, $s1, $s2 | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Complete (C):
  Write output result to physical register
  Notify reservation stations of dependent instructions that the physical register is ready

## Slide 14: MIPS R10K – Pipeline
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $t0, $s1, $s2 | F | De | Di | S | X | C | R |  | 
map table |  | 
$t0 | P1 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10, P5
reservation stations |  |  | 
func | insn | rs | rt
add |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
add $t0, $s1, $s2 | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
add $t0, $s1, $s2
Retire (R):
  Stall if not at head of reorder buffer
  Free old register
  Free reorder buffer entry
  If store instruction, write data to memory
  Handle any exceptions

## Slide 15: MIPS R10K – Example
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P5 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P1, P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready

## Slide 16: MIPS R10K – Example
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P1 | !rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* | lw $t0, 0($s0) | P6+ | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready
assume branch prediction
= not taken

## Slide 17: MIPS R10K – Example
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De |  |  |  |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P1 | !rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne | bne $t0, $s1, DEST | P1- | P4+
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
bne $t0, $s1, DEST |  | 
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready

## Slide 18: MIPS R10K – Example
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X |  |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S |  |  |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di |  |  |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P1 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P2, P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t1, $t0, -1 | P1- | 
bne | bne $t0, $s1, DEST | P1- | P4+
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
*assume 3 cycles to execute lw, else 1 cycle
+ means register ready, - means not ready

## Slide 19: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X |  |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S |  |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S |  |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P2 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t1, $t0, -1 | P1- | 
bne | bne $t0, $s1, DEST | P1- | P4+
lw* |  |  | 
sub | sub $t0, $s1, $s2 | P4+ | P0+
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
+ means register ready, - means not ready

## Slide 20: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X |  |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S |  |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S |  |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S |  |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di |  |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P2 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P8, P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t1, $t0, -1 | P1- | 
bne | bne $t0, $s1, DEST | P1- | P4+
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
+ means register ready, - means not ready

## Slide 21: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C |  |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S |  |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S |  |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X |  |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di |  |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P8 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P7, P10
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t0, $t0, 16 | P2- | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
lw $t0, 0($s0) | P1 | P5
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
+ means register ready, - means not ready

## Slide 22: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t0, $s0, 4 | P6+ | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready

## Slide 23: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | C |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | R |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | X |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | S |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | !rdy
$t1 | P3 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready

## Slide 24: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C | R |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | C | R |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | R | R |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | X | C |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | S | X |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | !rdy
$t1 | P3 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready

## Slide 25: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C | R |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | C | R | R |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | R | R | R |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | X | C | R |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | S | X | C |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | rdy
$t1 | P3 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5, P9
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready

## Slide 26: MIPS R10K – Example
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C | R |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | C | R | R |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | R | R | R | R |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | X | C | R | R | R |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | S | X | C | R | R | R |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | rdy
$t1 | P3 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5, P9, P1, P2, P8
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
+ means register ready, - means not ready

## Slide 27: MIPS R10K – Speculation
Misspeculation or interrupt/exception?
  Physical registers written out-of-order (C), but that’s ok: no arch reg file
  Can free written registers and restore old ones by manipulating map table and free list
    Don’t need to touch physical register file
    Serial rollback using rd and old rd fields

## Slide 28: MIPS R10K – Speculation
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P7 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t0, $s0, 4 | P6+ | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready
assume branch misprediction!
revert from youngest insn

## Slide 29: MIPS R10K – Speculation
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S |  |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | = |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P8 | !rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P7, P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi | addi $t0, $s0, 4 | P6+ | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
addi $t0, $s0, 4 | P7 | P8
+ means register ready, - means not ready
assume branch misprediction!
revert from youngest insn

## Slide 30: MIPS R10K – Speculation
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X |  |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X |  |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C |  |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | = |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | = |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P2 | rdy
$t1 | P3 | !rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P8, P7, P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
addi $t1, $t0, -1 | P3 | P9
sub $t0, $s1, $s2 | P2 | P1
addi $t0, $t0, 16 | P8 | P2
+ means register ready, - means not ready
assume branch misprediction!
revert from youngest insn

## Slide 31: MIPS R10K – Speculation
*assume 3 cycles to execute lw, else 1 cycle
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C |  |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | = |  |  |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | = |  |  |  |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | = |  |  |  |  |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | = |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
map table |  | 
$t0 | P1 | rdy
$t1 | P9 | rdy
$s0 | P6 | rdy
$s1 | P4 | rdy
$s2 | P0 | rdy
free list
P3, P2, P8, P7, P10, P5
reservation stations |  |  | 
func | insn | rs | rt
addi |  |  | 
bne |  |  | 
lw* |  |  | 
sub |  |  | 
reorder buffer |  | 
insn | rd | old
bne $t0, $s1, DEST |  | 
+ means register ready, - means not ready

## Slide 32: MIPS R10K – Takeaways
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
lw $t0, 0($s0) | F | De | Di | S | X | X | X | C | R |  |  |  |  |  |  |  | 
bne $t0, $s1, DEST |  | F | De | Di | S | S | S | S | X | C | R |  |  |  |  |  | 
addi $t1, $t0, -1 |  |  | F | De | Di | S | S | S | X | C | R | R |  |  |  |  | 
sub $t0, $s1, $s2 |  |  |  | F | De | Di | S | X | C | R | R | R | R |  |  |  | 
addi $t0, $t0, 16 |  |  |  |  | F | De | Di | Di | S | X | C | R | R | R |  |  | 
addi $t0, $s0, 4 |  |  |  |  |  | F | De | De | Di | S | X | C | R | R | R |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Takeaways:
  In-order stages: F, De, Di, R
  Out-of-order stages: S, X, C
  Changes to register mappings are in-order (Di and R)
  In-order stages stall while out-of-order stages wait

## Slide 33: Superscalar Processors
Step-by-step topics:
Scoreboard:
  Dynamic scheduling for enabling OoO execution
  Analogy: Can work on different projects simultaneously, but only one installation of LLVM is allowed in the system at any moment, so projects that need newer versions must wait for older projects to finish
MIPS R10K:
  Register renaming for eliminating WAR/WAW hazards
  Reorder buffer for handling speculation/precise state
  Analogy: Each version of LLVM is installed to a temp directory, with a symbolic link to the most recent version

## Slide 34: Exercise
When and which physical registers to free?
  Free _____ when add retires
  Free _____ when nor retires
  Free _____ when sub retires
  Free _____ when ori retires
 | MapTable |  |  |  | FreeList |  | Raw insns |  | Renamed insns
 | $t1 | $t2 | $t3 |  |  |  |  |  | 
 | p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add $t1,$t3,$t2 |  | add p4,p3,p2
 | p4 | p2 | p3 |  | p5,p6,p7 |  | nor $t3,$t1,$t2 |  | nor p5,p4,p2
 | p4 | p2 | p5 |  | p6,p7 |  | sub $t3,$t3,$t2 |  | sub p6,p5,p2
 | p4 | p2 | p6 |  | p7 |  | ori $t1,$t1,4 |  | ori p7,p4,4
p1
p3
p5
p4
time