## Slide 1: ECE/CS 552: Shared Memory and Coherence
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Shared Memory
Programming model for implicit communication
  Between different threads in the same process
shared
T0 private
T0 store
Tn load
physical memory
virtual memory P0
T0 private
Tn private

## Slide 3: Shared Memory
Programming model for implicit communication
  Between different processes
shared
private
shared
Pn private
P0 private
store
load
P0
Pn
physical memory
virtual memory

## Slide 4: Shared-Memory CMP
Focus on shared-memory CMPs
  Shared memory: all physical memory is accessible to all CPU cores
  Usually assume symmetric multiprocessors
    All CPU cores are alike
Shared memory idealisms
  Fully shared memory: usually nonuniform latency
  Single-cycle latency: approximate with cache hierarchy
  No contention: approximate with private caches
  Instantaneous propagation of writes: cache coherence required
Notes: Different flavors of chip multiprocessors exist, but we’ll be focusing on ones that assume a shared memory model, so all physical memory is accessible to all CPU cores and threads. We’ll generally also assume symmetric multiprocessors, where all the cores are alike, or homogeneous. So there are a few key idealisms that we strive for when building a shared-memory CMP. The first is that all physical memory is accessible to all cores, which is usually supported but comes at a cost of nonuniform latency, which I’ll elaborate on in a coming slide. The next idealisms are to achieve single-cycle memory access latency and no contention or interference from other threads currently executing on the system. We can approximately approach these goals by constructing a cache hierarchy with private caches, as I’ll show in the next slide. And the last idealism, which will be the main focus of this lecture, is that when one thread modifies a shared memory location, this modification should be instantaneously visible to all other threads. This is the job of the cache coherence protocol.

## Slide 5: Shared-Memory CMP
L1-I cache
L1-D cache
unified I/D
L2 cache
L1-I cache
L1-D cache
unified I/D
L2 cache
L1-I cache
L1-D cache
unified I/D
L2 cache
main memory
shared L3 cache
private L1, L2 caches

## Slide 6: UMA vs. NUMA

## Slide 7: Cache Coherence Problem
X: 37
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51
X: 51
Main Memory
t1: Load X=51
t2: Store X=37
assume write-back,
write-allocate cache
wrong value!
t3: Load X=51

## Slide 8: Cache Coherence Problem
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51 37
X: 51
Main Memory
t1: Load X=51
t2: Store X=37
wrong value!
t3: Load X=51
t5: Load X=51
t4: Evict X
assume write-back,
write-allocate cache
the role of the
cache coherence protocol

## Slide 9: Cache Coherence Protocol
Enforces the following for private caches:
Write Serialization: At any moment in time, only one processor can modify a memory block, and all processors agree on who it is (single-writer, multiple-reader invariant).
Write Propagation: Any processors that read the memory block immediately after a modification must observe the new value (data-value invariant).

## Slide 10: Cache Coherence Protocol
Another way to think about it:
A global logical time must be imposed upon all reads and writes to a memory block.
  Can trivially achieve by serializing all accesses, whether read or write (e.g., Modified-Invalid protocol).
  Can do better by allowing reads to occur in parallel (e.g., Modified-Shared-Invalid protocol).

## Slide 11: Cache Coherence Protocol
Caches coherence operates at block granularity
Assume write-back, write-allocate caches for rest of discussion
  Store misses must fetch the entire block first
  Evicting a dirty block writes its entire contents to memory (even untouched words)
  Without cache coherence, modified values are only visible after eviction
  With cache coherence, modified values are visible immediately

## Slide 12: Cache Coherence Protocols
Snooping-based coherence
Caches snoop (i.e., observe) all read/write requests (and their responses) to memory and other caches via broadcasting.
Directory-based coherence
Read/write requests (and their responses) are point-to-point; a separate directory structure must be referenced first to see who has copies of the data.
Advanced: ECE/CS 757

## Slide 13: Cache Coherence Protocols
Update-based protocols
Each cache is responsible for keeping its own blocks updated to the latest value.
Invalidation-based protocols
Each cache that modifies a block is responsible for notifying every other cache about the change (i.e., by invalidating the other caches’ stale copies).
Focus on snooping coherence with invalidation-based protocols (e.g., MI, MSI)

## Slide 14: Cache Coherence Protocols
A cache coherence protocol is implemented as a system of FSMs:
Each cache and memory employs a controller, which maintains a state for each block it contains and based on external events (e.g., requests, responses) from the upper and lower levels of the memory hierarchy, the controller transitions to a new state for the block and performs any actions associated with the transition (which may trigger new events)
Focus on cache controller FSMs

## Slide 15: MI Protocol
States:
Modified (M) state: Reads and writes allowed; cache has only copy of block
Invalid (I) state: Block is not cached
Events/Actions:
Load: read request from core to cache
Store: write request from core to cache
Evict: removal of block from cache
BusRdX: exclusive (write) request from cache to memory
BusReply: send block to requesting cache
BusWB: send block to memory
M
I
Store / --
Load / BusRdX
Load / --
BusRdX / BusReply
Store / BusRdX
Evict / BusWB
external event / cache action

## Slide 16: MI Protocol
Bus
P1
P2
A: 0
A [I]: --
A [I]: --
Main Memory
M
I
Store / --
Load / BusRdX
Load / --
BusRdX / BusReply
Store / BusRdX
Evict / BusWB

## Slide 17: MI Protocol
Bus
P1
P2
A: 0
A [I M]: 0 1
A [I]: --
Main Memory
t1: Store A=1
t2: BusRdX A
t3: BusReply A
M
I
Store / --
Load / BusRdX
Load / --
BusRdX / BusReply
Store / BusRdX
Evict / BusWB

## Slide 18: MI Protocol
Bus
P1
P2
A: 0
A [I M]: 0 3
A [I]: --
Main Memory
t1: Store A=1
t2: BusRdX A
t3: BusReply A
t4: Store A=2
t5: Load/Store A=3
M
I
Store / --
Load / BusRdX
Load / --
BusRdX / BusReply
Store / BusRdX
Evict / BusWB

## Slide 19: MI Protocol
Bus
P1
P2
A: 0
A [M I]
A [I M]: 3
Main Memory
t1: Store A=1
t2: BusRdX A
t3: BusReply A
t4: Store A=2
t6: Load A
t7: BusRdX A
cache sends data instead of memory, since it has the most up-to-date value
t8: BusReply A
M
I
Store / --
Load / BusRdX
Load / --
BusRdX / BusReply
Store / BusRdX
Evict / BusWB
invalidates other cache that is in M state
t5: Load/Store A=3

## Slide 20: MSI Protocol
Problem with MI protocol: Only one reader at a time
States:
Modified (M) state: Reads and writes allowed; cache has only copy of block
Shared (S) state: Only reads allowed; cache has one of multiple copies of block
Invalid (I) state: Block is not cached
New Events/Actions:
BusRd: read (shared) request from cache to memory
BusInv: exclusive (write) request from cache to memory, but cache already has read-only copy of block

## Slide 21: MSI Protocol
I
Load / BusRd
S
Bus
A [I]
A: 0
P2
A [I]
P1
1: Load A
2: BusRd A
3: BusReply A
A [I S]: 0

## Slide 22: MSI Protocol
I
Load / BusRd
S
Load / --
BusRd / --
Bus
A [I]
A: 0
P2
A [S]: 0
P1
1: Load A
2: BusRd A
3: BusReply A
A [I S]: 0
4: Load A

## Slide 23: MSI Protocol
I
Load / BusRd
S
Load / --
BusRd / --
Evict / --
Bus
A [I]
A: 0
P2
A [S]: 0
P1
A [S]: 0
A [S I]
Evict A

## Slide 24: MSI Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
Evict / --
Load, Store / --
BusRdX / --
A [S]: 0
Bus
A [I]
A: 0
P2
A [S I]: 0
P1
1: Store A
A [I M]: 0 1
2: BusRdX A
3: BusReply A

## Slide 25: MSI Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
Evict / --
BusRd / BusReply, BusWB
Load, Store / --
BusRdX / --
Bus
A [M]: 1
A: 0
P2
A [I]
P1
1: Load A
2: BusRd A
3: BusReply A
A [I S]: 1
A [M S]: 1
A: 0 1
4: BusWB A
memory gets the latest value of A too

## Slide 26: MSI Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
Evict / --
BusRd / BusReply, BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / --
Bus
A [S]: 1
A: 1
P2
A [S]: 1
P1
1: Store A
aka “Upgrade”
2: BusInv A
A [S M]: 2
A [S I]
how is BusInv different from BusRdX?
don’t need to get data from memory

## Slide 27: MSI Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
BusRdX / BusReply
Evict / --
BusRd / BusReply, BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / --
Bus
A [I]
A: 1
P2
A [M]: 2
P1
1: Store A
2: BusRdX A
3: BusReply A
A [M I]: 2
A [I M]: 3

## Slide 28: MSI Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
Evict / --
BusRd / BusReply, BusWB
Evict / BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / --
Bus
A [M]: 3
A: 1
P2
A [I]
P1
1: Evict A
2: BusWB A
A [M I]: 3
A: 1 3
BusRdX / BusReply

## Slide 29: MSI Protocol
Current State | Event |  |  |  |  | 
 | Load | Store | Evict | BusRd | BusRdX | BusInv
I | BusRd → S | BusRdX → M |  | → I | → I | → I
S | → S | BusInv → M | → I | → S | → I | → I
M | → M | → M | BusWB → I | BusReply BusWB → S | BusReply → I | 
action
→ next state

## Slide 30: Exercise
Modified-Shared-Invalid (MSI) Protocol
Store / BusRdX
I
Load / BusRd
S
Load / --
BusRd / --
M
Evict / --
BusRd / BusReply, BusWB
Evict / BusWB
Load, Store / --
Store / BusInv
BusRdX, BusInv / --
BusRdX / BusReply
why no BusWB too?
other cache in M eventually will write-back

## Slide 31: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
Bus
0, 0
B
A
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
(2000)
(2004)

## Slide 32: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
0, 5
0, 0
B
0, 0
A
Store 5
Load 0
Load 0

## Slide 33: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
0, 5
B
0, 0
A
Evict 0, 5

## Slide 34: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
0, 5
B
1, 0
A
Evict 1, 0
Store 1
1, 0

## Slide 35: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
1, 0
B
A
10, 0
Store 10
Load 1

## Slide 36: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
1, 0
B
A
10, 0
1, 3
Evict 1, 3
Store 3
1, 3

## Slide 37: Exercise
With write-back, write-allocate caches and coherence disabled, show how it’s possible for the memory contents at addresses 2000 and 2004 (same block) to be 10 and 0 after executing this multithreaded program:
# thread A
addi $t0, $zero, 2000
lw $t1, 0($t0)
...
addi $t2, $t1, 1
sw $t2, 0($t0)
...
addi $t3, $t1, 3
sw $t3, 4($t0)
...
# thread B
addi $t0, $zero, 2000
lw $t1, 4($t0)
...
addi $t1, $t1, 5
sw $t1, 4($t0)
...
lw $t2, 0($t0)
...
addi $t2, $t2, 9
sw $t2, 0($t0)
...
Bus
10, 0
B
A
Evict 10, 0