## Slide 1: ECE/CS 552: Consistency and SIMD
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Cache Coherence Problem
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,40,…
Main Memory
assume write-back,
write-allocate L1 cache

## Slide 3: Cache Coherence Problem
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,40,…
X: 51,40,…
Main Memory
1: Load X[0]=51
assume write-back,
write-allocate L1 cache

## Slide 4: Cache Coherence Problem
X: 51,37,…
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,40,…
X: 51,40,…
Main Memory
1: Load X[0]=51
2: Store X[1]=37
assume write-back,
write-allocate L1 cache
wrong value!
3: Load X[1]=40

## Slide 5: Cache Coherence Problem
X: 51,37,…
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,40,…
X: 51,40,…
Main Memory
1: Load X[0]=51
2: Store X[1]=37
assume write-back,
write-allocate L1 cache
3: Load X[1]=40
4: Evict X

## Slide 6: Cache Coherence Problem
---
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,37,…
X: 51,40,…
Main Memory
1: Load X[0]=51
2: Store X[1]=37
assume write-back,
write-allocate L1 cache
3: Load X[1]=40
4: Evict X

## Slide 7: Cache Coherence Problem
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 51,37,…
X: 22,40,…
Main Memory
1: Load X[0]=51
2: Store X[1]=37
assume write-back,
write-allocate L1 cache
3: Load X[1]=40
5: Store X[0]=22
4: Evict X
6: Evict X

## Slide 8: Cache Coherence Problem
A block X can exist in multiple private caches at any given moment. If one core modifies X, unless other cores are immediately made aware of this change, the other cores may read the stale (wrong) contents of X.
Bus
P1
P2
X: 22,40,…
---
Main Memory
1: Load X[0]=51
2: Store X[1]=37
assume write-back,
write-allocate L1 cache
3: Load X[1]=40
5: Store X[0]=22
4: Evict X
6: Evict X
wrong value of X[1]!

## Slide 9: Coherence and Consistency
Coherence: ordering of multiple cores’ reads and writes to one memory location.
Enforces that accesses to memory location are ordered as if they were performed in some sequential order
Consistency: ordering of multiple cores’ reads and writes to all memory locations.
Sequential consistency (SC) model: Enforces that accesses to all memory locations are ordered as if they were performed in some sequential order
Relaxed consistency models exist to improve performance

## Slide 10: Sequential Consistency
To achieve sequential consistency, it should appear as if:
Intra-thread program order: Each individual core’s reads and writes occur in program order.
Inter-thread serialization: All memory reads and writes from all cores are globally serialized.
load X
load Y
load X
store Y
store X
load Y
store X
store Y
only writes have to be serialized;
reads can happen in parallel
Inter-thread write atomicity: All memory writes are globally serialized and all cores agree on the order.

## Slide 11: SC Example
// P2
B = *x / 2;
...
*y = 5;
C = *x / 2;
// P1
*x = 8;
A = *y;
// init
*x = 0; *y = 0;
Possible result with SC: (A=0, C=0)?
No

## Slide 12: SC Example
// P2
B = *x / 2;
...
*y = 5;
C = *x / 2;
// P2
B = *x / 2;
...
*y = 5;
C = B;
// P1
*x = 8;
A = *y;
// init
*x = 0; *y = 0;
Possible result with SC: (A=0, C=0)?
No
compiler:
common subexpression elimination
(A=0, C=0)
SC violation!

## Slide 13: SC Example
// P2
B = *x * 2;
...
*y = 5;
C = *x * 2;
// P1
*x = 8;
A = *y;
// init
*x = 0; *y = 0;
Possible result with SC: (A=0, C=0)?
No
// P2
B = *x / 2;
...
*y = 5;
C = *x / 2;
(A=0, C=0)
SC violation!
out-of-order processor