## Slide 1: ECE/CS 552: Consistency and SIMD
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Forecast
Sequential consistency
SIMD
MISD

## Slide 3: Coherence and Consistency
Coherence: ordering of multiple cores’ reads and writes to one memory location.
Enforces that accesses to memory location are ordered as if they were performed in some sequential order
Consistency: ordering of multiple cores’ reads and writes to all memory locations.
Sequential consistency (SC) model: Enforces that accesses to all memory locations are ordered as if they were performed in some sequential order
Relaxed consistency models exist to improve performance

## Slide 4: Sequential Consistency
To achieve sequential consistency, it should appear as if:
Intra-thread program order: Each individual core’s reads and writes occur in program order.
Inter-thread serialization: All memory reads and writes from all cores are globally serialized.
load X
load Y
load X
store Y
store X
load Y
store X
store Y

## Slide 5: SC Example 1
// P2
B = *x * 2;
...
*y = 5;
C = *x * 2;
// P1
*x = 8;
A = *y;
// init
*x = 0; *y = 0;
Possible result with SC: (A=0, C=0)?
No

## Slide 6: SC Example 1
// P2
B = *x * 2;
...
*y = 5;
C = *x * 2;
// P1
*x = 8;
A = *y;
// init
*x = 0; *y = 0;
Possible result with SC: (A=0, C=0)?
No
// P2
B = *x * 2;
...
*y = 5;
C = B;
compiler:
common subexpression elimination
(A=0, C=0)
SC violation!

## Slide 7: SC Example 2
Possible result with SC: (A=B=C=2)?
No
// P2
C = *y;
*x = C;
// P1
A = *x;
B = *x;
if(A == B)
*y = 2;
// init
A = 0; B = 0; *x = 1; *y = 0;

## Slide 8: SC Example 2
Possible result with SC: (A=B=C=2)?
No
// P1
A = *x;
B = *x;
if(A == B)
*y = 2;
// init
A = 0; B = 0; *x = 1; *y = 0;
// P1
A = *x;
B = A;
if(A == B)
*y = 2;
// P1
A = *x;
B = A;
*y = 2;
compiler:
common subexpression elimination
compiler:
static true
// P2
C = *y;
*x = C;

## Slide 9: SC Example 2
Possible result with SC: (A=B=C=2)?
No
// P1
A = *x;
B = A;
*y = 2;
// init
A = 0; B = 0; *x = 1; *y = 0;
// P1
*y = 2;
A = *x;
B = A;
compiler:
independent of previous instructions
// P2
C = *y;
*x = C;
(A=B=C=2)
SC violation!

## Slide 10: SC Example 3
Possible assertion fail with SC?
No
// P2
if(*y != 0) {
A = *x;
assert(A != 0);
}
// P1
*x = 1;
*y = 1;
// init
*x = 0; *y = 0;
// P2
if(*y != 0) {
A = *x;
assert(A != 0);
}
out-of-order execution
with branch prediction
(assertion fail)
SC violation!

## Slide 11: SC Example 4
Possible result with SC: (A=7,B=0)?
No
// P1
while(*y == 0);
*z = 1;
A = *x;
// P0
*x = 7;
*y = 3;
// init
*x = 0; *y = 0; *z = 0;
// P5
while(*z == 0);
B = *y;

## Slide 12: SC Example 4
Possible result with SC: (A=7,B=0)?
No
// init
*x = 0; *y = 0; *z = 0;
P0
0, 0, 0
P1
0, 0, 0
P2
P3
P4
P5
0, 0, 0
// P0
*x = 7;
*y = 3;
// P1
while(*y == 0);
*z = 1;
A = *x;
// P5
while(*z == 0);
B = *y;
P1
7, 0, 0
P5
7, 0, 0
// P0
*x = 7;
*y = 3;
P0
7, 0, 0

## Slide 13: SC Example 4
Possible result with SC: (A=7,B=0)?
No
// init
*x = 0; *y = 0; *z = 0;
P0
7, 0, 0
P1
7, 0, 0
P2
P3
P4
P5
7, 0, 0
// P0
*x = 7;
*y = 3;
// P1
while(*y == 0);
*z = 1;
A = *x;
// P5
while(*z == 0);
B = *y;
network congestion
P1
7, 3, 0
// P0
*x = 7;
*y = 3;
P0
7, 3, 0
P0
7, 3, 1
P5
7, 0, 1
// P1
while(*y == 0);
*z = 1;
A = *x;
P1
7, 3, 1
(A=7, B=0)
SC violation!

## Slide 14: Sequential Consistency
To achieve sequential consistency, it should appear as if:
Intra-thread program order: Each individual core’s reads and writes occur in program order.
Inter-thread serialization: All memory reads and writes from all cores are globally serialized.
load X
load Y
load X
store Y
store X
load Y
store X
store Y
only writes have to be serialized;
reads can happen in parallel
Inter-thread write atomicity: All memory writes are globally serialized and all cores agree on the order.
  If a core writes a new value, all cores must acknowledge the write before any core is allowed to read it (coherence acknowledgements)
  Tell compiler not to reorder loads/stores (volatile)
  Allow for out-of-order execution, but double-check loads at retire stage (replay)
  Stall younger memory operations (fences)

## Slide 15: Volatile
Language declaration that allows the programmer to tell the compiler that an external entity (e.g., another thread, I/O device) may modify the memory location, so must be conservative and limit optimizations.
volatile int *x = ...;
*x = A;
...
B = *x;
compiler must assume that *x can be modified by someone else anytime

## Slide 16: SC Example 2 – Fixed
Possible result with SC: (A=B=C=2)?
No
// P2
C = *y;
*x = C;
// init
A = 0; B = 0;
volatile *x = 1; volatile *y = 0;
no more SC violation!
// P1
A = *x;
B = *x;
if(A == B)
*y = 2;

## Slide 17: Replay
MIPS R10K performs stores in-order at retire (R). Allow loads to be performed out-of-order at execute (X), but must replay them in-order at retire (R) to make sure their values have not changed since then. If the value has changed, flush and re-execute dependent instructions.
insn \ cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw $t0, 0($s0) | F | De | Di | S | S | S | S | X | C | R |  | 
lw $t1, 0($s1) |  | F | De | Di | S | X | C | R | R | R | R | 
add $t2, $t1, $t0 |  |  | F | De | Di | S | S | S | S | X | C | R
(1) perform load 0($s1)
(2) perform load 0($s0)
(3) replay load 0($s1)

## Slide 18: SC Example 3 – Fixed
Possible assertion fail with SC?
No
// P2
if(*y != 0) {
A = *x;
assert(A != 0);
}
// P1
*x = 1;
*y = 1;
// init
*x = 0; *y = 0;
out-of-order execution
with branch prediction
replay load (A=1)
no more SC violation!

## Slide 19: Memory Fences/Barriers
Special instructions to manually enforce intra-thread ordering of loads/stores, in case we do not want to change our OoO hardware implementation.
mfence: All prior loads and stores in this thread (in program order) must be globally acknowledged before proceeding.
lfence: All prior loads in this thread (in program order) must be globally acknowledged before proceeding.
sfence: All prior stores in this thread (in program order) must be globally acknowledged before proceeding.

## Slide 20: SC Example 3 – Fences
Possible assertion fail with SC?
No
// P2
if(*y != 0) {
lfence;
A = *x;
assert(A != 0);
}
// P1
*x = 1;
sfence;
*y = 1;
// init
*x = 0; *y = 0;

## Slide 21: Coherence Acknowledgements
When a core modifies a value and transitions to the modified (M) state, all other cores must first acknowledge that they have been invalidated before any of them are allowed to read the new value.
For snooping-based coherence, acknowledgements are implied since it is assumed that all cores are watching the common bus

## Slide 22: SC Example 4 – Fixed
Possible result with SC: (A=7,B=0)?
No
// init
*x = 0; *y = 0; *z = 0;
P0
7, 3, 0
P2
P3
P4
P5
7, 0, 0
// P0
*x = 7;
*y = 3;
// P1
while(*y == 0);
*z = 1;
A = *x;
// P5
while(*z == 0);
B = *y;
stalls here until all cores have acknowledged the new value of y
P5
7, 3, 0
P1
7, 0, 0
P1
7, 3, 0

## Slide 23: SC Example 4 – Fixed
Possible result with SC: (A=7,B=0)?
No
// init
*x = 0; *y = 0; *z = 0;
P0
7, 3, 1
P1
7, 3, 1
P2
P3
P4
P5
7, 3, 1
// P0
*x = 7;
*y = 3;
// P1
while(*y == 0);
*z = 1;
A = *x;
// P5
while(*z == 0);
B = *y;
no more SC violation!

## Slide 24: Flynn’s Taxonomy
Michael J. Flynn, Very High-Speed Computing Systems, Proc. IEEE, 1966.
SISD (Single Instruction – Single Data)
One instruction operating on one data location
SIMD (Single Instruction – Multiple Data)
One instruction operating on multiple data locations
MISD (Multiple Instruction – Single Data)
Multiple instructions operating on one data location
MIMD (Multiple Instruction – Multiple Data)
Multiple instructions operating on multiple data locations

## Slide 25: SIMD
Vector (Superword) Instructions:
conventional add r1, r2, r3
vector add vrA, vrB, vrC
vrA.1 | = | vrB.1 | + | vrC.1
vrA.2 |  | vrB.2 |  | vrC.2
vrA.3 |  | vrB.3 |  | vrC.3
vrA.4 |  | vrB.4 |  | vrC.4
r1 | = | r2 | + | r3

## Slide 26: Vector (Superword) Instructions
Vector registers are typically composed of multiple smaller registers.
e.g., Intel 128-bit SSE:
70 different instructions/operations
8 128-bit registers that can be accessed as:
  Two 64-bit integers or double-precision floating-point
  Four 32-bit integers or single-precision floating-point
  Eight 16-bit short integers
  Sixteen 8-bit chars
r0 | r1 | r2 | r3 | vrA
r4 | r5 | r6 | r7 | vrB
r8 | r9 | r10 | r11 | vrC
r12 | r13 | r14 | r15 | 
r16 | r17 | r18 | r19 | 

## Slide 27: Vector (Superword) Instructions
Loop unrolling:
for (i = 0; i < n; i += 4) {
a[i] = b[i] + c[i];
a[i+1] = b[i+1] + c[i+1];
a[i+2] = b[i+2] + c[i+2];
a[i+3] = b[i+3] + c[i+3];
}
for (i = 0; i < n; i += 1) {
a[i] = b[i] + c[i];
}
Loop fusion:
for (i = 0; i < n; i += 1) {
a[i].x = b[i].x + c[i].x;
a[i].y = b[i].y + c[i].y;
a[i].z = b[i].z + c[i].z;
}
for (i = 0; i < n; i += 1)
a[i].x = b[i].x + c[i].x;
...
for (i = 0; i < n; i += 1)
a[i].y = b[i].y + c[i].y;
...
for (i = 0; i < n; i += 1)
a[i].z = b[i].z + c[i].z;

## Slide 28: Vector (Superword) Instructions
VS
SW1: | a = b + c; d = e + f; g = h + i;
SW2: | j = a * l; k = d * m;
SW1
SW2
I1: I2: I3: | a = b + c; d = e + f; g = h + i;
I4: I5: | j = a * l; k = d * m;
I1
I2
I3
I4
I5
superword-level parallelism
instruction-level parallelism
Needs register packing/unpacking
Less flexible (e.g., same operations)
More dynamic instructions fetched and executed
Superscalar cost for same performance

## Slide 29: Vector (Superword) Instructions
VS
SW1: | a = b + c; d = e + f; g = h + i;
SW2: | j = a * l; k = d * m;
SW1
SW2
I1: I2: I3: | a = b + c; d = e + f; g = h + i;
I4: I5: | j = a * l; k = d * m;
I1
I2
I3
I4
I5
superword-level parallelism
instruction-level parallelism
Needs register packing/unpacking
Less flexible (e.g., same operations)
More dynamic instructions issued
Superscalar cost for same performance
An analogy:
Buy-one-get-one-free (BOGO) deals vs. membership discount.
BOGO is less flexible (infrequent, same item), but getting membership is expensive and often underutilized.

## Slide 30: Single-Instruction Multiple-Threads (SIMT)
Graphics Processing Units (GPUs)
Shader cores that exploit compute-intensive, massive data parallelism
Devote more transistors to processing rather than caching and flow control
Being used for general-purpose use (GPGPUs) in high-performance computing applications
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 31: GPUs
Threads perform the same computations
  Unify the fetch and decode logic
[J. Hensley, AMD]

## Slide 32: GPUs
There are many threads
  Stamp out many of these multiprocessors
[J. Hensley, AMD]

## Slide 33: GPUs
There are many, many threads
  Lots of time-multiplexing
[J. Hensley, AMD]

## Slide 34: MISD
Streaming Architectures:
e.g., Streaming big data analytics:
IBM stream computing
Apache Spark streaming

## Slide 35: Exercise
Insert the minimum number of store fences and load fences to ensure SC:
Assume inter-thread write atomicity support
// P1
while(*y == 0);
*z = 1;
A = *x;
// P0
*x = 7;
*y = 3;
// init
*x = 0; *y = 0; *z = 0;
// P5
while(*z == 0);
B = *y;

## Slide 36: Exercise
Insert the minimum number of store fences and load fences to ensure SC:
Assume inter-thread write atomicity support
// P1
while(*y == 0);
lfence;
*z = 1;
A = *x;
// P0
*x = 7;
sfence;
*y = 3;
// init
*x = 0; *y = 0; *z = 0;
// P5
while(*z == 0);
lfence;
B = *y;