## Slide 1: ECE/CS 552: Integer Multiplication and Division
Boone Severson
Lecture notes based in part on slides created by Joshua San Miguel, Mikko Lipasti, Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Forecast
Integer multiplication
  Array multiplier
  Multicycle multiplier
  Booth’s encoding
Integer division
  Restoring division
  Non-restoring division

## Slide 3: Multiplication
Flashback to 3rd grade
  Multiplier
  Multiplicand
  Partial products
  Final sum
e.g., 8 × 9
  8 + 0<<1 + 0<<2 + 8<<3 = 72
How wide is the result?
  log(n x k) = log(n) + log(k)
  32b x 32b = 64b result
Multiplicand |  |  |  | 1 | 0 | 0 | 0
Multiplier |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 4: Multiplication
Multiplicand |  |  |  | A3 | A2 | A1 | A0
Multiplier |  |  | x | B3 | B2 | B1 | B0
 |  |  |  | A3B0 | A2B0 | A1B0 | A0B0
 |  |  | A3B1 | A2B1 | A1B1 | A0B1 | 
 |  | A3B2 | A2B2 | A1B2 | A0B2 |  | 
 | A3B3 | A2B3 | A1B3 | A0B3 |  |  | 
p7 | p6 | p5 | p4 | p3 | p2 | p1 | p0

## Slide 5: Array Multiplier
Adding all partial products simultaneously using an array of basic cells
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Full Adder
Ai Bj Sin Cin
Cout Sout
Ai ,Bj

## Slide 6: Array Multiplier
+ Conceptually straightforward
- Fairly expensive hardware
- Integer multiplies are relatively rare
[Source: J. Hayes, Univ. of Michigan]
16b × 16b
A15B0+A14B1
A0B0

## Slide 7: Multicycle Multiplier
Multicycle multipliers
  Accumulate the partial products row-by-row
  Iterate through each bit of the multiplier:
    If 1, add the multiplicand
    Shift the multiplicand and move on to the next bit

## Slide 8: Multicycle Multiplier

## Slide 9: Multicycle Multiplier
0000 1000
1001
0000 0000
0000 1000
1001
0000 1000
1001
1 = enable add
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 10: Multicycle Multiplier
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0001 0000
100
0000 1000
0 = disable add

## Slide 11: Multicycle Multiplier
0010 0000
10
0000 1000
0 = disable add
0100 0000
1
0100 1000
1 = enable add
1000 0000
0100 1000
done
but only need to add 32 bits at a time
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 12: Improved Multiplier
only need 32-bit multiplicand register
Multiplier
combine multiplier with product reg

## Slide 13: Improved Multiplier
1000
0000 1001
Multiplier
1000
1000 1001
1 = enable add
Multiplier
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 14: Improved Multiplier
1000
0100 0100
0 = disable add
Multiplier
1000
0010 0010
0 = disable add
Multiplier
1000
1001 0001
1 = enable add
Multiplier
1000
0100 1000
done
Multiplier
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | x | 1 | 0 | 0 | 1
 |  |  |  | 1 | 0 | 0 | 0
 |  |  | 0 | 0 | 0 | 0 | 
 |  | 0 | 0 | 0 | 0 |  | 
 | 1 | 0 | 0 | 0 |  |  | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
number of adds = number of 1s in multiplier

## Slide 15: Signed Multiplication
So far, only unsigned multiplication
Option 1:
  Convert multiplier/multiplicand to positive integers
  Multiply
  Compute sign, then convert product accordingly
Option 2:
  Implement the improved multiplier
  Arithmetic right shift instead of logical
  If multiplier negative, on last multiplier bit, subtract multiplicand instead of adding

## Slide 16: Booth’s Multiplier
Recall grade school trick
  When multiplying by 9:
    Multiply by 10 (easy, just shift digits left), then subtract once
    e.g., 123456 x 9 = 123456 x (10 – 1) = 1234560 – 123456
    Converts addition of six partial products to one shift and one subtraction
Booth’s multiplier applies the same principle
  e.g., Multiplying by 00001111000 (120 in decimal) is equivalent to multiplying by 00010000000 – 00000001000 (128 – 8 in decimal)
  Booth’s Encoding: Convert each run of 1s in the multiplier to a difference of powers of 2

## Slide 17: Booth’s Multiplier
Multiplier bits | Current bit | Previous bit | Description | Operation
00001111000 | 1 | 0 | Begins run of 1s (rising edge) | Subtract (-)
00001111000 | 1 | 1 | Middle of run of 1s | Nothing (0)
00001111000 | 0 | 1 | End of run of 1s (falling edge) | Add (+)
00001111000 | 0 | 0 | Middle of run of 0s | Nothing (0)
From right (least significant) to left (most significant) bit:
Booth’s encoding: 000+000-000
e.g., Multiplying by 00001111000 (= 00010000000 – 00000001000)

## Slide 18: Booth’s Multiplier
Positive multiplier:
  -6 x 6 = -36
  1010 x 0110
  Multiplier 0110 in Booth’s encoding is +0-0
1111 1010 | x 0 | 0000 0000
 | Final Sum: | 
Positive multiplier:
  -6 x 6 = -36
  1010 x 0110
  Multiplier 0110 in Booth’s encoding is +0-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
 | Final Sum: | 
Positive multiplier:
  -6 x 6 = -36
  1010 x 0110
  Multiplier 0110 in Booth’s encoding is +0-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
 | Final Sum: | 
Positive multiplier:
  -6 x 6 = -36
  1010 x 0110
  Multiplier 0110 in Booth’s encoding is +0-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
1101 0000 | x +1 | + 1101 0000
 | Final Sum: | 1101 1100 (-36)
number of adds/subs = number of falling/rising edges

## Slide 19: Division
Again, back to 3rd grade (74 ÷ 8 = 9 rem 2)
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 20: Restoring Division
How does hardware know if divisor fits at each bit position?
  Subtract: remainder = remainder – divisor
  Then check if remainder ≥ 0
  If not, add the divisor back to restore the remainder
  Then shift to the next bit position

## Slide 21: Restoring Division
Dividend

## Slide 22: Restoring Division
00001000 00000000
00000000 01001010
Dividend
00001000 00000000
11111000 01001010
remainder ≥ 0? no
remainder – divisor
Dividend
0
00001000 00000000
remainder ≥ 0? no
remainder + divisor
Dividend
0
00000000 01001010
restore
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 23: Restoring Division
00000000 01000000
00000000 01001010
0000
Dividend
00000000 01000000
00000000 00001010
00001
remainder ≥ 0? yes
Dividend
remainder – divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 24: Restoring Division
00000000 00100000
00000000 00001010
00001
Dividend
00000000 00100000
11111111 11101010
00001
remainder ≥ 0? no
Dividend
remainder – divisor
00000000 00100000
00000000 00001010
000010
remainder ≥ 0? no
restore
Dividend
remainder + divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 25: Restoring Division
00000000 00001000
00000000 00001010
0000100
Dividend
00000000 00001000
00000000 00000010
00001001
remainder ≥ 0? yes
Dividend
remainder – divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder
done

## Slide 26: Improved Division
Skip the first subtraction
  Remainder is initially 0, so no use subtracting
  Shift first, then subtract
    Need to undo extra shift in the end
Hardware similar to multiplier
  Can store quotient in remainder register
  Only need 32-bit ALU

## Slide 27: Improved Division
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder
00000000 01001010
00001000
Dividend/Quotient

## Slide 28: Improved Division
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder
00000000 10010100
00001000
Dividend/Quotient
left-shift in a 0

## Slide 29: Improved Division
11111000 10010100
00001000
remainder ≥ 0? no
Dividend/Quotient
remainder – divisor
00000000 10010100
00001000
remainder ≥ 0? no
restore
Dividend/Quotient
remainder + divisor
00000001 00101000
00001000
remainder ≥ 0? no
left-shift in a 0
Dividend/Quotient
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 30: Improved Division
00001001 01000000
00001000
skip ahead
Dividend/Quotient
00000001 01000000
00001000
remainder ≥ 0? yes
Dividend/Quotient
remainder – divisor
00000010 10000001
00001000
remainder ≥ 0? yes
Dividend/Quotient
left-shift in a 1
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 31: Improved Division
00001010 00000100
00001000
skip ahead
Dividend/Quotient
00000010 00000100
00001000
remainder ≥ 0? yes
Dividend/Quotient
remainder – divisor
00000100 00001001
00001000
remainder ≥ 0? yes
Dividend/Quotient
left-shift in a 1
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 32: Improved Division
00000100 00001001
00001000
done
Dividend/Quotient
00000010 00001001
00001000
done
Dividend/Quotient
right-shift
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 33: Non-Restoring Division
Restoring division takes 2 ALU cycles per bit position
  1 cycle to check for divisibility (i.e., subtraction)
  1 cycle to restore if needed (i.e., addition)
Non-restoring division: reduce to 1 cycle per bit position
  First, subtract: remi = remi-1 – divisor
  If remi < 0, don’t restore yet:
    Correct remi+1 = ((remi + divisor) << 1) – divisor
    = (remi + divisor)*2 – divisor = remi + divisor
  Thus if remi < 0, add instead of subtract next:
    remi+1 = remi + divisor

## Slide 34: Non-Restoring Division
00000000 01001010
00001000
Dividend/Quotient
00000000 10010100
00001000
Dividend/Quotient
left-shift in a 0
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 35: Non-Restoring Division
11111000 10010100
00001000
remainder ≥ 0? no
Dividend/Quotient
remainder – divisor
11110001 00101000
00001000
remainder ≥ 0? no
next: add
Dividend/Quotient
left-shift in a 0
remainder – divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 36: Non-Restoring Division
11111001 00101000
00001000
next: add
Dividend/Quotient
remainder + divisor
remainder ≥ 0? no
11110010 01010000
00001000
next: add
remainder ≥ 0? no
Dividend/Quotient
left-shift in a 0
remainder + divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 37: Non-Restoring Division
11111001 01000000
00001000
next: add
skip ahead
Dividend/Quotient
00000001 01000000
00001000
remainder ≥ 0? yes
next: add
Dividend/Quotient
remainder + divisor
00000010 10000001
00001000
remainder ≥ 0? yes
next: sub
Dividend/Quotient
left-shift in a 1
remainder + divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 38: Non-Restoring Division
11111010 00000100
00001000
next: add
skip ahead
Dividend/Quotient
00000010 00000100
00001000
remainder ≥ 0? yes
next: add
Dividend/Quotient
remainder + divisor
00000100 00001001
00001000
remainder ≥ 0? yes
next: sub
Dividend/Quotient
left-shift in a 1
remainder + divisor
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 39: Non-Restoring Division
00000100 00001001
00001000
done
Dividend/Quotient
00000010 00001001
00001000
done
Dividend/Quotient
right-shift
 |  |  |  |  |  |  |  | 1 | 0 | 0 | 1 | Quotient
Divisor | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Dividend
 |  |  |  | - | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 |  |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 |  | 
 |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 
 |  |  |  |  |  |  | - | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  | 1 | 0 | Remainder

## Slide 40: Exercise – Booth’s Multiplier
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110
multiplier

## Slide 41: Exercise – Booth’s Multiplier
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110
  Multiplier 1110 in Booth’s encoding is 00-0
1111 1010 | x 0 | 0000 0000
 | Final Sum: | 
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110
  Multiplier 1110 in Booth’s encoding is 00-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
 | Final Sum: | 
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110
  Multiplier 1110 in Booth’s encoding is 00-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
 | Final Sum: | 
Negative multiplier:
  -6 x -2 = 12
  1010 x 1110
  Multiplier 1110 in Booth’s encoding is 00-0
1111 1010 | x 0 | 0000 0000
1111 0100 | x –1 | 0000 1100
1110 1000 | x 0 | 0000 0000
1101 0000 | x 0 | + 0000 0000
 | Final Sum: | 0000 1100 (12)