## Slide 1: Virtual Memory
Discussion 11/06/24

## Slide 2: Why Virtual Memory?
Programmer and Hardware have different views of memory
VM reconciles this
Multiple programs running can now view memory as if they are the only programs running

## Slide 3: Physical Memory – Processor’s View
PM – Actual Memory modules
  In the range of 4 GB (Sometimes even lesser)
  Never 4 GB per process
  Not 2^16 B per process
PM is less than what the programs can access
Addresses have 1:1 mapping to the bytes /words in the PM

## Slide 4: Program’s View
Contiguous array of memory (0 – 2^64)
Program thinks it has a lot of memory
  But the program might not even use all of this memory!
Need to go where it goes in the PM
Same address can map to different locations in the PM
  Look at Synonyms and Homonyms problem in adv cache
Program 1
Program 2
PM

## Slide 5: Mapping VM  PM
We cannot have every byte in the VM map to some arbitrary address in the PM – this requires a huge table of mappings (large memory)
Instead divide the VM into pages (typically 4KB)
  Each page aligns with the page size
PM is divided into Frames (Like caches)
  PM is a cache to VM
Mapping mechanism – Page Table
  For each VM, where does it map to in the PM. OS does this
Different processes have a different Page Tables

## Slide 6: Page Tables
For a 2GB PM, 4 GB VM, 4 KB Page Size
  How many page frames (PM) and how many entries in each page table?
  #Frames = 2GB/4GB = 2^19 frames
  1 entry for each page in the VM = 4 GB/4KB = 2^20 = 1M entries
Where is the missing memory? On the disk
  VM significantly exceeds the size of PM

## Slide 7: Translating VA  PA
VPN used to index into the PT
  This tells the frame # corresponding to the VPN
{Physical frame #/PPN, Page Offset} is used to access the PM
LSB bits do not change!!
4-entry PT, 16 bit VA space and 20 bit PA space
  0x1F
  0x3F
  0x23
  0x17
  Where does 0xF0F0 map to?
16 bit VA space and 4 entry PT => MSB 2 bits are PN and remaining 14 bits are page offset
11|11 0000 1111 0000
00|00 0000 0001 1111
{0001 0111 (since it access 0x17 (index 3)) , page offset} – 0x5F0F0

## Slide 8: Flat PT
For entry per page in the entire VA space, even for those pages that are never accessed by the program!
  For eg., (4GB/4KB)*4B = 4 MB – but the process might not even use the entire 4 GB
Entry has Frame # + Bits that says if the page is accessible (protection bits/bits that say if it is present in the PM or not)
Overall size = (Sizeof(VM)/Page Size) * Size of each PTE
Very large PT size
If VM is 64 bit, then PT is 2^32 x 4GB!!

## Slide 9: Flat PT
8B Entry (64 bit PA space)
4 KB page size
Two processes
2 GB PM
32 bit VA
Process 1 uses only 1 MB of the addr space
Process 2 uses 1 GB
What is the total size of Page Tables?
2 page tables are needed
2 x (2^32/2^12) x 8 = 16 x 2^20 = 16MB
How much mem the processor uses does not matter – it needs to have an entry for each possible page in the VA space. Does not matter how much PM we have (what matters is the size of entry)

## Slide 10: Multi Level PTs
Size of flat PT proportional to the address space
32 bit VA – Flat PT is couple MB even if the program uses only few KB
64 bit???? Too big (So flat PT cannot be used)
Multi level PTs – reduce the PT size
  Uses bits to index into the PT
  Avoid the use of PT for the region between heap and stack

## Slide 11: Multi Level PTs
Page Number (PN) partitioned into inner and outer PN
Outer PN used to index into the outer PT – tells where to find the inner PT. Use the inner PN to index into the inner PT to find the frame#
Same entries in the inner PT and have added an extra layer. How does it save space?
For eg; 4 bit offset and 4 bit PN
  4 X 4 entries + some outer PT
  If there is an used large part, then we can mark that the entry is not valid and eliminate that PT. So we have only one large outer PT and smaller inner PTs

## Slide 12: Multi Level PTs
32 bit addr space
4 KB page
1024 entry outer PT, 1024 entry inner PT
PT entry is 8 bytes
Program uses VM at 0x.. 0x00010 000
and 0xFFFF0000 … 0xFFFF FFFF
What is the size? Flat and 2 level PTs?
Flat PT – 2^32 pages/2^12 bytes in each page = 2^20 entries x 8 = 8 MB
2 level – address has 12 bit offset, 10 bit inner and outer PN
Outer PT = 2^10 X 8 bytes per entry = 8 KB for outer PT
Which of these entries point to actual inner PT?
Split the 20 bit PN into 10 bit groups –
0000 0000 00 | 00 0001 0000 same outer PN – only entry 0 points to inner PT
FFFF0 – FFFFF same outer PN – only last outer PTE points
Out of 1024 entries only 2 point to the inner PTs = 2X 1024X8 = 16 KB
Which is 24 KB - this is why we use multi-level PTs

## Slide 13
Memory access time for VA  PA translation?
Say LW R1, 4(R2) // this is the VA
Need a memory access for all loads? Costs a lot more
  1 cycle to compute VA, 1 cycle to acess cache, 10 cycles to access mem, 90 % hit rate, PTE are in memory
  How many cycles for this instr for a 3 level PT?
  Say the PTE are now cached? How many cycles now?
Need a mem access for each load if the PT is in mem
PTE in mem and not in cache? 1 cycle to find addr + 10 cycles to access inner most PT + actual cache access 1 + 3X10 + 1 + 0.1X10 = 33 cycles (30 only to access the PTs)
PTE in cache - 1 cycle + 3X(1+0.1X10) + (1+0.1X10) = 9 cycles
MOTIVATION FOR TLB

## Slide 14: Translation Look-aside Buffer (TLB)
Cache for the address translations
  But relatively smaller than the cache
TLB only stores the final translation and not the intermediate PTNs
So we need only one access to get the data
What if there is a TLB miss?
  Software miss handling by the OS (like a tree or hashing structure)
  Hardware miss handling (processor can automatically read the PTs and update the TLB. Faster at the expense of hardware complexity )

## Slide 15: 4 Level PT
64 bit VA
64 bit Page size
8B PTE
Program uses only 0.. 4GB
Size of flat and 4 level PT?
2^64/2^16 = 2^48 entries
Flat = 2^48 X 8 = 2^51 B
48 bit PN is split into 4 pieces of 12 bits
Now figure out how many inner PTs we have
4 GB mem = 2^32 bytes = 2^16 x 2^16 (2^16 pages)
1 inner most PT has 2^12 entries – so it covers 2^12 pages
To cover 2^16 pages, we need 2^4 of these inner most PTs (so we have 16 inner most PTs)
How many PTs at the next level do we need to point to these? (these can also have 2^12 entries and this is only 2^4 – so we need only 1)
Outer most has 4096 entries (only one has a valid pointer)
Next level has 4096 also has only 1 valid
Next level has 16 entries that point to inner most PTs
1 + 1 + 1 + 16 = 19 (2^12 X 2^3 X 19)