## Slide 1: ECE/CS 552: Final Exam Review
Boone Severson
Based on notes from Joshua San Miguel

## Slide 2: Announcements
Final exam: Tue 12/17
  12:25 - 2:25 PM in Van Hise 494
  See Final Exam Info on Canvas
  Final exam review: Now, 12/10
Please take the time to complete course eval:
  https://heliocampusac.wisc.edu/

## Slide 3: Announcements
Phase 3 due Monday 12/16
  12/17 means -20%
  12/18 means -40%
Extra Credit due Monday 12/16
  Not graded if Phase 3 incomplete or late
  Talk to Shreya/Boone for expectations before starting to avoid surprises

## Slide 4: Final Exam
See Weekly Outline in Canvas
  Lectures 12 – 21
    Textbook Readings
    PDF handouts
    Class exercises
    Homework
    Quizzes

## Slide 5: Caches
Placement, Replacement, Write Policy
Hit, Miss (Cold/Compulsory, Conflict, Capacity)
Set-associativity (Direct-mapped, 2+ way)
Global/Local miss rates, Average memory access time

## Slide 6: Physical/Virtual Addresses
Why Virtualize Addresses?
1 level & multi-level Page Tables
Address translation
  VPNPPN, POFS
TLB cache for PTEs; Reach
PIPT, VIVT, VIPT caches (synonym/homonym)
Code/Heap/Stack pages

## Slide 7: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
TLB (8-entry, 2-way set-associative) |  | 
Set | 18-bit Tag | 8-bit PPN
0 | 0x18042 | 0xAB
 | 0x30601 | 0x42
1 | 0x30804 | 0xCD
 | 0x2C0A0 | 0x02
2 | 0x06040 | 0x54
 | 0x30202 | 0x81
3 | 0x20810 | 0x90
 | 0x30402 | 0xE3

## Slide 8: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
TLB (8-entry, 2-way set-associative) |  | 
Set | 18-bit Tag | 8-bit PPN
0 | 0x18042 | 0xAB
 | 0x30601 | 0x42
1 | 0x30804 | 0xCD
 | 0x2C0A0 | 0x02
2 | 0x06040 | 0x54
 | 0x30202 | 0x81
3 | 0x20810 | 0x90
 | 0x30402 | 0xE3
If VIVT: VA = 1100000010000000101 0000100 010100
| t | s | o |

## Slide 9: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
TLB (8-entry, 2-way set-associative) |  | 
Set | 18-bit Tag | 8-bit PPN
0 | 0x18042 | 0xAB
 | 0x30601 | 0x42
1 | 0x30804 | 0xCD
 | 0x2C0A0 | 0x02
2 | 0x06040 | 0x54
 | 0x30202 | 0x81
3 | 0x20810 | 0x90
 | 0x30402 | 0xE3
If PIPT:
VPN = 0xC080A
VPN = 110000001000000010 10
| t | s |
If VIVT: VA = 1100000010000000101 0000100 010100
| t | s | o |

## Slide 10: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
TLB (8-entry, 2-way set-associative) |  | 
Set | 18-bit Tag | 8-bit PPN
0 | 0x18042 | 0xAB
 | 0x30601 | 0x42
1 | 0x30804 | 0xCD
 | 0x2C0A0 | 0x02
2 | 0x06040 | 0x54
 | 0x30202 | 0x81
3 | 0x20810 | 0x90
 | 0x30402 | 0xE3
If PIPT:
VPN = 0xC080A
VPN = 110000001000000010 10
| t | s |
PPN = 0x81
If VIVT: VA = 1100000010000000101 0000100 010100
| t | s | o |

## Slide 11: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
TLB (8-entry, 2-way set-associative) |  | 
Set | 18-bit Tag | 8-bit PPN
0 | 0x18042 | 0xAB
 | 0x30601 | 0x42
1 | 0x30804 | 0xCD
 | 0x2C0A0 | 0x02
2 | 0x06040 | 0x54
 | 0x30202 | 0x81
3 | 0x20810 | 0x90
 | 0x30402 | 0xE3
If PIPT:
VPN = 0xC080A
VPN = 110000001000000010 10
| t | s |
PPN = 0x81
PA = 0x81114
PA = 1000000 1000100 010100
| t | s | o |
If VIVT: VA = 1100000010000000101 0000100 010100
| t | s | o |

## Slide 12: Caches and Virtual Memory
Load word for 32-bit virtual address 0xC080A114 on a system with 4KiB pages. The cache is 3-way set-associative with 64B blocks and 24KiB capacity. Given TLB contents below, what are the set, offset and tag bits used to access the cache, if (a) VIVT? (b) PIPT?
If PIPT:
VPN = 0xC080A
VPN = 110000001000000010 10
| t | s |
PPN = 0x81
PA = 0x81114
PA = 1000000 1000100 010100
| t | s | o |
If VIVT: VA = 1100000010000000101 0000100 010100
| t | s | o |
If VIPT, would synonyms be a problem?
Yes, since:
set+offset bits = 13 > page offset bits = 12

## Slide 13: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7

## Slide 14: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0

## Slide 15: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0
S2 = 1

## Slide 16: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0
S2 = 1
S3 = 1

## Slide 17: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0
S2 = 1
S3 = 1
SP = 1

## Slide 18: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0
S2 = 1
S3 = 1
SP = 1

## Slide 19: ECC
One or two bit-flips may have occurred in this SECDED codeword: W8W7W6W5W4W3W2W1 = 01101011. Recover the original data.
W6 has flipped: original data b4b3b2b1 = 1000
S3S2S1, SP | Bit flipped?
000, 0 | none
001, 1 | W1
010, 1 | W2
011, 1 | W3
100, 1 | W4
101, 1 | W5
110, 1 | W6
111, 1 | W7
000, 1 | W8
non-zero, 0 | double bit-flip
Syndrome, Parity | 
S1 | W1⊕W3⊕W5⊕W7
S2 | W2⊕W3⊕W6⊕W7
S3 | W4⊕W5⊕W6⊕W7
SP | W8⊕…⊕W1
Codeword | 
W1 | C1 = b1⊕b2⊕b4
W2 | C2 = b1⊕b3⊕b4
W3 | b1
W4 | C3 = b2⊕b3⊕b4
W5 | b2
W6 | b3
W7 | b4
W8 | P = W1⊕…⊕W7
S1 = 0
S2 = 1
S3 = 1
SP = 1

## Slide 20: Superscalar, OoO, MIPS R10K
Fewer stalls, parallelism, more efficiency
R10K (R10K-like)
  Register Renaming (hazards)
    Map Table, Free List
  Multiple pipelines (OoO)
  Reorder Buffer (speculation)
  Pipeline Diagrams, purpose of each stage, where/why stalls happen

## Slide 21: MIPS R10K
Fetch
Decode
Dispatch
PC
RS
RS
RS
Map Table
& Free List
Physical
Register File
Complete
Retire
Issue
Reorder Buffer
Execute
Dispatch (Di):
Get + set MT
Push entry into ROB
Allocate RS
Otherwise, stall
Issue (S):
Read from reg file, if operands ready
Allocate functional unit
Free RS
Otherwise, wait
Complete (C):
Write result to reg file
Set ready flag in MT
Set ready flag in RSs
Retire (R):
Stall, if not at head of ROB
Push old reg to Free List
Pop entry from ROB

## Slide 22: MIPS R10K
Assume MIPS R10K-like processor with one-cycle X stage and infinite hardware. What is the minimum number of ROB entries required such that the program never stalls due to a full ROB?
{ I1: and $t1, $s5, $t1
I2: sub $s1, $s1, $s0
I3: lw $t1, 0($s2) } × 100
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
I1 | F | De | Di | S | X | C | R |  |  |  |  |  |  |  |  | 
I2 |  | F | De | Di | S | X | C | R |  |  |  |  |  |  |  | 
I3 |  |  | F | De | Di | S | X | C | R |  |  |  |  |  |  | 
I1 |  |  |  | F | De | Di | S | S | X | C | R |  |  |  |  | 
I2 |  |  |  |  | F | De | Di | S | X | C | R | R |  |  |  | 
I3 |  |  |  |  |  | F | De | Di | S | X | C | R | R |  |  | 
I1 |  |  |  |  |  |  | F | De | Di | S | S | X | C | R |  | 
I2 |  |  |  |  |  |  |  | F | De | Di | S | X | C | R | R | 
I3 |  |  |  |  |  |  |  |  | F | De | Di | S | X | C | R | R
I1 |  |  |  |  |  |  |  |  |  | F | De | Di | S | S | X | C
I2 |  |  |  |  |  |  |  |  |  |  | F | De | Di | S | X | C
I3 |  |  |  |  |  |  |  |  |  |  |  | F | De | Di | S | X

## Slide 23: MIPS R10K
Assume MIPS R10K-like processor with one-cycle X stage and infinite hardware. What is the minimum number of ROB entries required such that the program never stalls due to a full ROB?
{ I1: and $t1, $s5, $t1
I2: sub $s1, $s1, $s0
I3: lw $t1, 0($s2) } × 100
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
I1 | F | De | Di | S | X | C | R |  |  |  |  |  |  |  |  | 
I2 |  | F | De | Di | S | X | C | R |  |  |  |  |  |  |  | 
I3 |  |  | F | De | Di | S | X | C | R |  |  |  |  |  |  | 
I1 |  |  |  | F | De | Di | S | S | X | C | R |  |  |  |  | 
I2 |  |  |  |  | F | De | Di | S | X | C | R | R |  |  |  | 
I3 |  |  |  |  |  | F | De | Di | S | X | C | R | R |  |  | 
I1 |  |  |  |  |  |  | F | De | Di | S | S | X | C | R |  | 
I2 |  |  |  |  |  |  |  | F | De | Di | S | X | C | R | R | 
I3 |  |  |  |  |  |  |  |  | F | De | Di | S | X | C | R | R
I1 |  |  |  |  |  |  |  |  |  | F | De | Di | S | S | X | C
I2 |  |  |  |  |  |  |  |  |  |  | F | De | Di | S | X | C
I3 |  |  |  |  |  |  |  |  |  |  |  | F | De | Di | S | X
The ROB should have at least 5 entries.

## Slide 24: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _________ [older/younger] instructions can erroneously _________ [read from/write to] registers that still have yet to be _________ [read/written] by _________ [older/younger] instructions.

## Slide 25: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _________ [older/younger] instructions can erroneously _________ [read from/write to] registers that still have yet to be _________ [read/written] by _________ [older/younger] instructions.
 | renamed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $t0, 0($t1) | lw P7, 0(P1) | F | De | Di | S | X | X | X | X | X | X | X | C | R |  |  | 
sub $t2, $t3, $t0 | sub P8, P3, P7 |  | F | De | Di | S | S | S | S | S | S | S | S | X | C | R | 
addi $t3, $t4, 1 | addi P9, P4, 1 |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R | R
sw $t4, 0($t1) | sw P4, 0(P1) |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R
sw $t5, 4($t1) | sw P5, 4(P1) |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R
ori $t6, $t6, 3 | ori P3, P6, 3 |  |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R

## Slide 26: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _________ [older/younger] instructions can erroneously _________ [read from/write to] registers that still have yet to be _________ [read/written] by _________ [older/younger] instructions.
 | renamed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $t0, 0($t1) | lw P7, 0(P1) | F | De | Di | S | X | X | X | X | X | X | X | C | R |  |  | 
sub $t2, $t3, $t0 | sub P8, P3, P7 |  | F | De | Di | S | S | S | S | S | S | S | S | X | C | R | 
addi $t3, $t4, 1 | addi P9, P4, 1 |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R | R
sw $t4, 0($t1) | sw P4, 0(P1) |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R
sw $t5, 4($t1) | sw P5, 4(P1) |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R
ori $t6, $t6, 3 | ori P3, P6, 3 |  |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R
frees P3

## Slide 27: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _________ [older/younger] instructions can erroneously _________ [read from/write to] registers that still have yet to be _________ [read/written] by _________ [older/younger] instructions.
 | renamed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $t0, 0($t1) | lw P7, 0(P1) | F | De | Di | S | X | X | X | X | X | X | X | C | R |  |  | 
sub $t2, $t3, $t0 | sub P8, P3, P7 |  | F | De | Di | S | S | S | S | S | S | S | S | X | C | R | 
addi $t3, $t4, 1 | addi P9, P4, 1 |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R | R
sw $t4, 0($t1) | sw P4, 0(P1) |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R
sw $t5, 4($t1) | sw P5, 4(P1) |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R
ori $t6, $t6, 3 | ori P3, P6, 3 |  |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R
frees P3
writes to P3

## Slide 28: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _________ [older/younger] instructions can erroneously _________ [read from/write to] registers that still have yet to be _________ [read/written] by _________ [older/younger] instructions.
 | renamed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $t0, 0($t1) | lw P7, 0(P1) | F | De | Di | S | X | X | X | X | X | X | X | C | R |  |  | 
sub $t2, $t3, $t0 | sub P8, P3, P7 |  | F | De | Di | S | S | S | S | S | S | S | S | X | C | R | 
addi $t3, $t4, 1 | addi P9, P4, 1 |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R | R
sw $t4, 0($t1) | sw P4, 0(P1) |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R
sw $t5, 4($t1) | sw P5, 4(P1) |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R
ori $t6, $t6, 3 | ori P3, P6, 3 |  |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R
frees P3
writes to P3
reads wrong P3

## Slide 29: MIPS R10K
In our MIPS R10K-like processor, old physical registers are freed at the end of the R stage. If they were freed at C instead, then _younger_ [older/younger] instructions can erroneously _write to_ [read from/write to] registers that still have yet to be ___read___ [read/written] by __older__ [older/younger] instructions.
 | renamed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $t0, 0($t1) | lw P7, 0(P1) | F | De | Di | S | X | X | X | X | X | X | X | C | R |  |  | 
sub $t2, $t3, $t0 | sub P8, P3, P7 |  | F | De | Di | S | S | S | S | S | S | S | S | X | C | R | 
addi $t3, $t4, 1 | addi P9, P4, 1 |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R | R
sw $t4, 0($t1) | sw P4, 0(P1) |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R | R
sw $t5, 4($t1) | sw P5, 4(P1) |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R | R
ori $t6, $t6, 3 | ori P3, P6, 3 |  |  |  |  |  | F | De | Di | S | X | C | R | R | R | R | R
frees P3
writes to P3
reads wrong P3

## Slide 30: Multiprocessors
In 552, R10K is top-performing core
  Instruction-Level Parallelism
Dennard scaling has forced the multicore era
Compute-Level vs Data-Level Parallelism
Concurrency vs Parallelism
Speedup – Amdahl’s Law
Multithreading
Simultaneous Multithreading (partition/pool)
Notes: SISD
SIMD
MISD
MIMD - TLP
ILP – superscalar
TLP - MIMD

## Slide 31: Shared-Memory CMP
L1-I cache
L1-D cache
unified I/D
L2 cache
L1-I cache
L1-D cache
unified I/D
L2 cache
L1-I cache
L1-D cache
unified I/D
L2 cache
main memory
shared L3 cache
private L1, L2 caches

## Slide 32: Shared-Memory CMP
NUMA vs UMA
Why coherence protocols?
  MI vs MSI
  Block granularity
  Snoop
Private Caches need Write Serialization & Write Propagation

## Slide 33: Consistency
Coherence vs Consistency
  Coherence: Ordering to 1 memory location
  Consistency: Ordering all reads/writes to all mem.
    Sequential Consistency (SC)
      Each core’s reads/writes occur in program order
      All cores’ memory accesses are globally serialized
    Manual Sequential Consistency?
      lfence, sfence, mfence
      volatile (C/C++)
    R10K Loads OoO (X), Stores in-order (R); Replay load (R)
    Coherence Acknowledgements

## Slide 34: Consistency
Two threads run on a shared-memory multiprocessor. There are no private caches, and all memory contents are initially 0.
Which of the following outcomes are possible assuming the multiprocessor supports sequential consistency?
[$s0] = 0 and [$s1] = 0
[$s0] = 0 and [$s1] = 1
[$s0] = 1 and [$s1] = 0
[$s0] = 1 and [$s1] = 1
Where do you need to insert fences to guarantee SC?
# thread A A0: ori $t0, $zero, 2000 A1: lw $s0, 0($t0) A2: lw $s1, 4($t0) | # thread B B0: ori $t0, $zero, 2000 B1: addi $t1, $zero, 1 B2: sw $t1, 4($t0) B3: sw $t1, 0($t0)

## Slide 35: Consistency
Two threads run on a shared-memory multiprocessor. There are no private caches, and all memory contents are initially 0.
Which of the following outcomes are possible assuming the multiprocessor supports sequential consistency?
[$s0] = 0 and [$s1] = 0
[$s0] = 0 and [$s1] = 1
[$s0] = 1 and [$s1] = 0
[$s0] = 1 and [$s1] = 1
Where do you need to insert fences to guarantee SC?
One between A1 and A2 and one between B2 and B3
# thread A A0: ori $t0, $zero, 2000 A1: lw $s0, 0($t0) A2: lw $s1, 4($t0) | # thread B B0: ori $t0, $zero, 2000 B1: addi $t1, $zero, 1 B2: sw $t1, 4($t0) B3: sw $t1, 0($t0)
i, ii, iv are possible

## Slide 36: Cache Coherence
Four threads run on a shared-memory multiprocessor with private caches that use the MSI coherence protocol. Without knowing the initial states of the caches, you observe the following sequence of memory accesses to a single block X.
What is the current coherence state of block X in each cache (M/S/I/Unknown) after this sequence of accesses?
 | Cache A | Cache B | Cache C | Cache D
Time 0 | Load X |  |  | 
Time 1 |  | Load X |  | 
Time 2 |  |  | Store X | 
Time 3 | Load X |  |  | 
State of Block X | Cache A | Cache B | Cache C | Cache D
Block X |  |  |  | 

## Slide 37: Cache Coherence
Four threads run on a shared-memory multiprocessor with private caches that use the MSI coherence protocol. Without knowing the initial states of the caches, you observe the following sequence of memory accesses to a single block X.
What is the current coherence state of block X in each cache (M/S/I/Unknown) after this sequence of accesses?
 | Cache A | Cache B | Cache C | Cache D
Time 0 | Load X |  |  | 
Time 1 |  | Load X |  | 
Time 2 |  |  | Store X | 
Time 3 | Load X |  |  | 
State of Block X | Cache A | Cache B | Cache C | Cache D
Block X | S |  |  | 

## Slide 38: Cache Coherence
Four threads run on a shared-memory multiprocessor with private caches that use the MSI coherence protocol. Without knowing the initial states of the caches, you observe the following sequence of memory accesses to a single block X.
What is the current coherence state of block X in each cache (M/S/I/Unknown) after this sequence of accesses?
 | Cache A | Cache B | Cache C | Cache D
Time 0 | Load X |  |  | 
Time 1 |  | Load X |  | 
Time 2 |  |  | Store X | 
Time 3 | Load X |  |  | 
State of Block X | Cache A | Cache B | Cache C | Cache D
Block X | S | I |  | 

## Slide 39: Cache Coherence
Four threads run on a shared-memory multiprocessor with private caches that use the MSI coherence protocol. Without knowing the initial states of the caches, you observe the following sequence of memory accesses to a single block X.
What is the current coherence state of block X in each cache (M/S/I/Unknown) after this sequence of accesses?
 | Cache A | Cache B | Cache C | Cache D
Time 0 | Load X |  |  | 
Time 1 |  | Load X |  | 
Time 2 |  |  | Store X | 
Time 3 | Load X |  |  | 
State of Block X | Cache A | Cache B | Cache C | Cache D
Block X | S | I | S | 

## Slide 40: Cache Coherence
Four threads run on a shared-memory multiprocessor with private caches that use the MSI coherence protocol. Without knowing the initial states of the caches, you observe the following sequence of memory accesses to a single block X.
What is the current coherence state of block X in each cache (M/S/I/Unknown) after this sequence of accesses?
 | Cache A | Cache B | Cache C | Cache D
Time 0 | Load X |  |  | 
Time 1 |  | Load X |  | 
Time 2 |  |  | Store X | 
Time 3 | Load X |  |  | 
State of Block X | Cache A | Cache B | Cache C | Cache D
Block X | S | I | S | I

## Slide 41: SIMD
Add 2 32-deep arrays into a 3rd
  Scalar
  for (int i=0; i<32; i++) c[i] = a[i] + b[i];
  Vector
  c = a + b;

## Slide 42: SIMT and MISD
SIMT GPUs
  Massively parallel threads
MISD
  Multiple computations on the same data

## Slide 43: Integer Multiplier
Multiplicand, Multiplier, Partial, Product
Array - huge
Compromise:
  Multicycle
  Improved multicycle
  Improved algorithm (Booth’s encoding)
Signed numbers
  Arithmetic Shift; Add or Subtract

## Slide 44: Divider
Dividend, Divisor, Quotient, Remainder
Multicycle and Improved Multicycle
Restoring
  Subtract; if remainder <0, Add back to restore
  Shift, repeat
Non-Restoring
  Subtract; if remainder <0, then Add next time
  Shift, repeat

## Slide 45: Floating Point
Floating point format:
  S: sign bit, E: exponent, F: fraction (mantissa)
  Value: (-1)S x 1.F x 2E
  e.g., 9.25 in decimal = 1.00101 x 23 in binary
  Fraction w/implicit 1 is called a Significand
  (-1)S x 1.F x 23; S=0; F=00101; E-7=3, E=10
S
E
F
S = sign | E = exp | F = fraction
0 | 1010 | 00101
normalized
(implicit/hidden leading 1)
usually biased e.g. bias = 7 E = 10

## Slide 46: IEEE754 Special Cases
Single Precision |  | Double Precision |  | Value
E | F | E | F | 
0 | 0 | 0 | 0 | zero
0 | nonzero | 0 | nonzero | denormalized
255 | 0 | 2047 | 0 | infinity
255 | nonzero | 2047 | nonzero | NaN (Not a Number)
Explore IEEE 754 @ https://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 47: Review – Ex 12/03 Q2
This program performs unsigned integer division of two 16-bit numbers: 19 ÷ 3 (in decimal).
L0: lui $t0, 3
L1: ori $t1, $zero, 19
L2: add $t2, $zero, $zero
L3: addi $t3, $zero, 16
L4: srl $t0, $t0, 1
L5: sll $t2, $t2, 1
L6: sltu $t7, $t1, $t0
L7: bne $t7, $zero, L10
L8: subu $t1, $t1, $t0
L9: ori $t2, $t2, 1
L10: addi $t3, $t3, -1
L11: bne $t3, $zero, L4
(a,b) Which registers contain quotient and remainder at the end?

## Slide 48: Review – Ex 12/03 Q2
This program performs unsigned integer division of two 16-bit numbers: 19 ÷ 3 (in decimal).
L0: lui $t0, 3
L1: ori $t1, $zero, 19
L2: add $t2, $zero, $zero
L3: addi $t3, $zero, 16
L4: srl $t0, $t0, 1
L5: sll $t2, $t2, 1
L6: sltu $t7, $t1, $t0
L7: bne $t7, $zero, L10
L8: subu $t1, $t1, $t0
L9: ori $t2, $t2, 1
L10: addi $t3, $t3, -1
L11: bne $t3, $zero, L4
(a,b) Which registers contain quotient and remainder at the end?
[$t2] = quotient, [$t1] = remainder
[$t1]: 0000000000010011
[$t0]: 0000000000000011
[$t2]:
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 0
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 00
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 0000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 00000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 0000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 00000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 000000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 0000000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 00000000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 000000000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
?
[$t2]: 0000000000000
[$t1]: 0000000000010011
[$t0]: -0000000000000011
[$t1] = 0000000000000111
[$t2]: 00000000000001
[$t1]: 0000000000000111
[$t0]: -0000000000000011
[$t1] = 0000000000000001
[$t2]: 000000000000011
[$t1]: 0000000000000001
[$t0]: -0000000000000011
?
[$t2]: 0000000000000110

## Slide 49: Review – Ex 12/03 Q2
This program performs unsigned integer division of two 16-bit numbers: 19 ÷ 3 (in decimal).
L0: lui $t0, 3
L1: ori $t1, $zero, 19
L2: add $t2, $zero, $zero
L3: addi $t3, $zero, 16
L4: srl $t0, $t0, 1
L5: sll $t2, $t2, 1
L6: sltu $t7, $t1, $t0
L7: bne $t7, $zero, L10
L8: subu $t1, $t1, $t0
L9: ori $t2, $t2, 1
L10: addi $t3, $t3, -1
L11: bne $t3, $zero, L4
(c) How many times is instruction L8 executed?

## Slide 50: Review – Ex 12/03 Q2
This program performs unsigned integer division of two 16-bit numbers: 19 ÷ 3 (in decimal).
L0: lui $t0, 3
L1: ori $t1, $zero, 19
L2: add $t2, $zero, $zero
L3: addi $t3, $zero, 16
L4: srl $t0, $t0, 1
L5: sll $t2, $t2, 1
L6: sltu $t7, $t1, $t0
L7: bne $t7, $zero, L10
L8: subu $t1, $t1, $t0
L9: ori $t2, $t2, 1
L10: addi $t3, $t3, -1
L11: bne $t3, $zero, L4
(c) How many times is instruction L8 executed?
2 times
[$t1]: 0000000000000001
[$t0]: -0000000000000011
?
Quotient [$t2]: 0000000000000110