## Slide 1: ECE/CS 552: Midterm Review
Boone Severson
Based on Notes from Joshua San Miguel

## Slide 2: Midterm
Midterm this Thursday 10/24 during class, in this room
  Closed book, pen-and-paper exam
  One hand-written cheat sheet allowed
  MIPS green card will be provided for you

## Slide 3: First Page of Midterm

## Slide 4
Core Instruction Set only
No Arithmetic Instructions
No Pseudoinstructions

## Slide 5: Endianness
State the contents of register $t1 depending on the endianness of the machine, after executing the following instructions:
Little-endian:
Big-endian:
lui $t0, 258
ori $t0, $t0, 772 # [$t0] = 0x01020304
sw $t0, 0($s0)
lbu $t1, 1($s0)

## Slide 6: Endianness
State the contents of register $t1 depending on the endianness of the machine, after executing the following instructions:
Little-endian:
  [$t1] = 0x3
Big-endian:
lui $t0, 258
ori $t0, $t0, 772 # [$t0] = 0x01020304
sw $t0, 0($s0)
lbu $t1, 1($s0)
Memory (little-endian) | 
([$s0] + 3) | 0x01
([$s0] + 2) | 0x02
([$s0] + 1) | 0x03
([$s0] + 0) | 0x04

## Slide 7: Endianness
State the contents of register $t1 depending on the endianness of the machine, after executing the following instructions:
Little-endian:
  [$t1] = 0x3
Big-endian:
  [$t1] = 0x2
lui $t0, 258
ori $t0, $t0, 772 # [$t0] = 0x01020304
sw $t0, 0($s0)
lbu $t1, 1($s0)
Memory (little-endian) | 
([$s0] + 3) | 0x01
([$s0] + 2) | 0x02
([$s0] + 1) | 0x03
([$s0] + 0) | 0x04
Memory (big-endian) | 
([$s0] + 3) | 0x04
([$s0] + 2) | 0x03
([$s0] + 1) | 0x02
([$s0] + 0) | 0x01

## Slide 8: Processor Data Path
Modify the data path below such that all branch targets are computed as PC = PC + BranchAddr instead.

## Slide 9: Processor Data Path
Modify the data path below such that all branch targets are computed as PC = PC + BranchAddr instead.

## Slide 10: Data Dependences
List all register dependences in the following program:
RAW
$t2: L1 → L2
$t0: L2  L3
L1: lw $t2, 4($t0)
L2: subi $t0, $t2, 72
L3: beq $t0, $t3, L1
L4: add $t0, $t2, $t3
WAR
$t0: L1 → L2
$t0: L3  L4
WAW
$t0: L2 → L4

## Slide 11: Data Forwarding
  lw $t0, 0($t1)
  lw $s1, 4($t0)
  add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume forwarding to EX and RF bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 12: Data Forwarding
  lw $t0, 0($t1)
  lw $s1, 4($t0)
  add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume forwarding to EX and RF bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
Cycle 7

## Slide 13: Branch Prediction
Consider a branch predictor that uses a BHT with 8 entries, each containing a 1-bit prediction (1=taken). Assume the current state of the BHT as shown below. You encounter a branch instruction at address PC=0x10001014, and it is found to be not taken; specify the following:
BHT index of this branch:
  5
Prediction for this branch:
  taken
Updated BHT entry value:
  0
index PC[4:2] | 1-bit prediction (1=taken)
0 | 0
1 | 1
2 | 1
3 | 0
4 | 1
5 | 1
6 | 0
7 | 0

## Slide 14: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2?
L3?
L5?
L1: | addi | $s2, $zero, 16
L2: | and | $s4, $s4, $s1
L3: | slt | $s6, $s1, $s2
L4: | beq | $s6, $s0, L7
 | <branch delay slot> | 
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 15: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2?
L3?
L5?
L1: | addi | $s2, $zero, 16
L3: | slt | $s6, $s1, $s2
L4: | beq | $s6, $s0, L7
L2: | and | $s4, $s4, $s1
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 16: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2? Yes
L3?
L5?
L1: | addi | $s2, $zero, 16
L3: | slt | $s6, $s1, $s2
L4: | beq | $s6, $s0, L7
L2: | and | $s4, $s4, $s1
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 17: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2? Yes
L3?
L5?
L1: | addi | $s2, $zero, 16
L2: | and | $s4, $s4, $s1
L4: | beq | $s6, $s0, L7
L3: | slt | $s6, $s1, $s2
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 18: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2? Yes
L3? No
L5?
L1: | addi | $s2, $zero, 16
L2: | and | $s4, $s4, $s1
L4: | beq | $s6, $s0, L7
L3: | slt | $s6, $s1, $s2
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 19: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2? Yes
L3? No
L5?
L1: | addi | $s2, $zero, 16
L2: | and | $s4, $s4, $s1
L3: | slt | $s6, $s1, $s2
L4: | beq | $s6, $s0, L7
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 20: Branch Delay Slots
Which of the instructions below can individually be legally removed from its current position in the program and placed into the branch delay slot instead? Ignore potential exceptions.
L2? Yes
L3? No
L5? Yes
L1: | addi | $s2, $zero, 16
L2: | and | $s4, $s4, $s1
L3: | slt | $s6, $s1, $s2
L4: | beq | $s6, $s0, L7
L5: | or | $s3, $s4, $s6
L6: | add | $s1, $s1, $s3
L7: | slt | $s3, $s2, $s5

## Slide 21: COD 4.65
Where do Stalls originate?
Decode
Full Forwarding to EX
RF Bypass
Predict not taken

## Slide 22: COD 4.65 Pipeline Terminology
What is a Stall?
  A D* stall is when the results of D transformed to a NOP for the ID/EX pipeline registers
  F* is different; ID/EX.wen = 0 prevents ID/EX from updating, so D will re-execute on the next clock
When will F Stall (F*)?
  F* will stall only when D* originates a stall

## Slide 23: COD 4.65
Where are Branches decided?
Decode
=
+
<<2
Full Forwarding to EX
RF Bypass
Predict not taken

## Slide 24: COD 4.65 Pipeline Terminology
What is a Flush?
  A flush is when an instruction in F is transformed into a NOP by muxing in 0’s and registering them in IF/ID pipeline registers (=)
When does full-forwarding, RF bypass, predict not-taken CPU Flush?
  Branches are determined in Decode, and the younger instruction in Fetch will be flushed if the branch is taken

## Slide 25: COD 4.65
Stall?
Full Forwarding to EX
RF Bypass
Predict not taken
add $t0, $t1, $t2
addi $s0, $t0, $s0
No. EX-to-EX Forwarding.

## Slide 26: COD 4.65
Full Forwarding to EX
RF Bypass
Predict not taken
No. $t0 result is in W, and will use WD RF bypass
Stall?
L1: add $t0, $s0, $s1
L2: addi $s0, $s0, 4
L3: addi $s1, $s1, -4
L4: beq $t0, $s2, L5

## Slide 27: COD 4.65
Full Forwarding to EX
RF Bypass
Predict not taken
Yes. Once for load-to-use on $s0, then twice for beq on $s1 (RF bypass).
Stall?
L1: lw $s0, 0($t0)
L2: add $s1, $t1, $s0
L3: beq $s1, $zero, L5

## Slide 28: Pipeline Diagrams
2 instructions cannot be in the same stage in the same clock
An instruction cannot stall after being executed
  e.g. D  D*
X, M, and W do not stall in COD 4.65 Full Forward, RF Bypass, Predict-not-taken CPU

## Slide 29: Pipeline
L1: sub $s4, $s2, $s3
L2: sw $s2, 8($s1)
L3: __w $s2, 0($s4)
L4: lw ___, 4(___)
L5: add $s1, $zero, $s5
L6: lw $s3, 0($s3)
L7: __w $s1, 0($s3)
L8: add $s2, $s1, $s2
Assume five-stage pipeline with forwarding to EX and RF bypassing support. Fill in the blanks such that the following sequence of instructions takes exactly 16 cycles to complete.

## Slide 30: Pipeline
L1: sub $s4, $s2, $s3
L2: sw $s2, 8($s1)
L3: __w $s2, 0($s4)
L4: lw ___, 4(___)
L5: add $s1, $zero, $s5
L6: lw $s3, 0($s3)
L7: __w $s1, 0($s3)
L8: add $s2, $s1, $s2
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16

## Slide 31: Pipeline
L1: sub $s4, $s2, $s3
L2: sw $s2, 8($s1)
L3: lw $s2, 0($s4)
L4: lw $s5, 4($s2)
L5: add $s1, $zero, $s5
L6: lw $s3, 0($s3)
L7: lw $s1, 0($s3)
L8: add $s2, $s1, $s2
Assume five-stage pipeline with forwarding to EX and RF bypassing support. Fill in the blanks such that the following sequence of instructions takes exactly 16 cycles to complete.

## Slide 32: Pipeline
L1: sub $s4, $s2, $s3
L2: sw $s2, 8($s1)
L3: lw $s2, 0($s4)
L4: lw $s5, 4($s2)
L5: add $s1, $zero, $s5
L6: lw $s3, 0($s3)
L7: lw $s1, 0($s3)
L8: add $s2, $s1, $s2
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
L1 | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
L2 |  | F | D | X | M | W |  |  |  |  |  |  |  |  |  | 
L3 |  |  | F | D | X | M | W |  |  |  |  |  |  |  |  | 
L4 |  |  |  | F | D* | D | X | M | W |  |  |  |  |  |  | 
L5 |  |  |  |  | F* | F | D* | D | X | M | W |  |  |  |  | 
L6 |  |  |  |  |  |  | F* | F | D | X | M | W |  |  |  | 
L7 |  |  |  |  |  |  |  |  | F | D* | D | X | M | W |  | 
L8 |  |  |  |  |  |  |  |  |  | F* | F | D* | D | X | M | W

## Slide 33: Happy Studying!
Piazza
E-mail
Wednesday Discussion
  3:30-4:30 PM in 209 Animal Science
Zoom (make an appointment!)